Early Porsche 911 Frequently Asked Questions

Version: 3.4

Last-modified: Thu 12 Dec 1996.

Copyright 1995,1996, Wade Guthrie. Permission is granted to copy and redistribute

this document so long as it is unmodified and the copyright remains in-tact.

Note: I use a lot of names that are trademarks in this FAQ. At no time should the use of a

trademarked name be construed as contesting the trademark. Those trademarks belong to their

respective trademark holders.

Disclaimer: The information in this FAQ is a compilation from various sources including the internet.

The author/maintainer does not guarantee any of the information found in this FAQ. Use this FAQ

AT YOUR OWN RISK and with your own judgement (in fact, this is pretty good advice for all the

information found on the internet).

Q0. What does this FAQ cover?

This FAQ was originally written to fill the need for, well, a FAQ on Porsche's 911 model. Though it

contains information for many of the later 911s and derivatives, it concentrates on the earlier

models. Eventually, I'd like to bisect this FAQ and give the late-model half to someone who is

better qualified to answer those questions. In the mean time, this FAQ covers the following:

1. Background

Q1.1. What's a 911?

Q1.2. What are the differences between the various 911s?

Q1.3. Okay, so how do I tell the difference between them?

Q1.4. But, Porsches are known for performance; how do the models differ?

Q1.5. What should the VIN or engine number look like for my car?

Q1.6. Why did the early 911s have two batteries?

2. Purchase

Q2.1. Which 911 Should I Get?

Q2.2. I want to buy a 911. For what should I look?

Q2.3. Does anyone have a checklist for potential 911 buyers?

3. Upkeep, Repair, and Parts

Q3.1. What are the classic problems / areas to check on 911s?

Q3.2. So, what's wrong with the 2.7 liter 911s?

Q3.3. Where can I get new and used parts for my 911?

Q3.4. At what pressure and temperature ranges should my 911 operate?

Q3.5. Where can I find a car seat for the rear seats of my 911?

Q3.6. Any other places I can look for 911 info?

Q1.1. What's a 911?

Yikes. Okay, in 1963 Porsche announced the 901, a car based on the venerable 356 model. The

car was renamed 911 because Peugeot had a copyright on all 3-digit car model numbers with a

zero in the middle. The 911 has gone on to become, arguably, the most popular car ever produced

by Porsche.

The 911 engine is an air cooled (or oil cooled) six cylinder opposed design (%). The cylinders bolt

onto the crankcase such that displacement increases are often achieved by replacing the pistons and

cylendars.

The body of the car was designed by Ferdinand "Butzi" Porsche (Ferry's son) while the engine was

designed by Ferdinand Piech (Dr. Porsche's nephew).

(%) It is not a boxer design. A boxer engine has not only a 180 degree layout, but has a flat

crankshaft arranged so that the matching pistons are at top-dead-center at the same time (so that

the pistons move, alternately, toward or away from each other).

Q1.2. What are the differences between the

various 911s?

There's *lots* of differences:

Numerous of body styles

Coupe. 4 seats (well, 2 and a couple postage stamps) and a hard roof. You know. . .a

COUPE

Targa. Like a coupe, but with a roll bar and a removable top. The earlier targas had soft

rear windows, but the later ones had glass.

Cabriolet. A full-on convertible.

Speedster. A version of convertible, but with a short windshield and a fiberglass tonneau

(the 356 speedster was different, but we're talking about 911s here).

Several trim and tune options.

T, E, S. The early years (the latest any of these were produced was 1977) cars in touring,

injected and super (also fuel injected) states of tune.

Carrera. For the earlier cars, this was the quickest standard customer car. After 1983, the

Carrera was the standard customer car.

SC. This was the standard car (there was also the turbo for some of theses years) between

1978 and 1983.

H, N. Rare models: 911RS Homologation (20 made in 1973) and a Euro model in 1976.

L. The one-year replacement for the 911S in the US.

R, RS, RSR. 911 in race trim. These cars are always rare and expensive.

Turbo. This one is, well, turbo charged.

Model Year Differences.

And, finally, there are the various changes over the different model years. Major Eras Include (the

names are, partly, my own):

1964-1968 short wheel base (SWB, 2211 mm to be exact). In contrast, the long wheel base

(LWB) is 2268 mm long.

1968-1973 early power. These 2.0, 2.2, and 2.4 liter 911s (my personal favorites) saw

either mechanical fuel injection or carburetors (actually, in 73.5, the 911 T was electronically

fuel injected).

1974-1977 middle-year 911s. These cars had the 2.7 liter engines that had a notoriously

short life span. This is the beginning of the crash bumpers (with the accordion sections at the

edges) and K-Jetronic fuel injection.

1978-1983 911SC. These 3.0 liter SCs are powerful, luxurious, and nearly bullet-proof.

1984-1989 Motronic Carreras. Like the 911SC, but with a 3.2 liter engine and Motronic

fuel injection.

1989-1994 964 (original 911 Carrera 2/4). These cars have the one-piece, all body color

bumpers and the engine cover that raises at 50 MPH to form a wing.

1994-today 993 (today's 911)

Note: Years given are model year. The model years start in August or September of the previous

year (example 1972 model year starts in September of 1971). Much of the research for this

document has been clouded by research materials not specifying whether they discussed calendar

year or model year.

More specific differences are given in table 1, below.

Q1.3. Okay, so how do I tell the difference

between them?

Well, you asked for it. . .

Short Wheel Base 1964-1968

1968 and earlier cars have a shorter wheelbase than the 911s built in 1969 and after (recognition

hint: the torsion bar tubes are right next to the SWB cars' rear wheel well -- there's a gap in the

LWB cars). Other accoutrements of the SWB cars are:

glass lens covered headlights,

exterior door handles that opened via an exposed push-button (rather than the flying-buttress

protection or trigger of later years),

no side marker reflectors,

Hella 128 fog lights mounted through the bottom half of the front bumper,

a vertical structural strip running under the rear engine grille,

sunroof models during these years had a drain slot above the rain gutter above the back side

windows,

And, in the interior:

chrome instrument bezels with green lettering,

ceiling-mounted rear-view mirror (1968 was as well, but it was break-away type)

a one piece under-dash knee guard,

pleated door pockets, and

push-buttons to open the doors from the inside.

Until 1971, non-S models had silver painted slotted steel wheels; S models had Fuchs alloy wheels.

911s before the 1967 model year had the '911' designation diagonally across the lower right corner

of the engine cover and the PORSCHE script in one piece (well, actually it was two pieces, but it

looked like one) on the bottom.

1964 2.0 liter

There were four 901 prototypes produced (serial numbers 13326, 13327, 13328, and 13330).

Porsche went on to build 125 first year (1964) 901 cars.

RECOGNITION TIPS:

The 1964 cars have no rocker-panel trim and and no model designation on the engine lid or on the

dash. Supporting clues are that 1966 and earlier 911s have wooden dash trim and open A-frame

window cranks.

1965 2.0 liter

RECOGNITION TIPS:

These cars look nearly identical to the 1966 cars. The things that separate these cars from the

1966s is in the interior. The 1965 cars have no wrap-around knee guard, aluminum backing on the

wood dash trim, or rubber shift boot (I think they were leather). Both years are similar in that they

have the rocker panel trim (this is not found on the 1964 cars), wooden dash trim, and open

A-frame window cranks.

OPTIONS:

A four speed transmission became standard mid-model year. Sunroof, tinted windshield, enamel

porsche crest on wheels, chrome plated steel wheels, gasoline heater (LHD models only), ambient

temperature gauge, driver's side vanity mirror on sun visor, recaro or ferrari seats (actually, both are

made by recaro), leather seats headrests

1966 2.0 liter

Weber carbs replace Solex mid-model year. S model introduced mid- model year. Fuchs wheels

introduced. Targa (with soft rear window) introduced. 911 introduced in US.

RECOGNITION TIPS:

These cars look nearly identical to the 1965 cars. The things that separate these cars from the

1966s is in the interior (see the 1965 description). Of course, if the car is an 'S' model, it has to be a

1966 or later. US models have all chrome vertical bumper guards (standard equipment) -- 911S

bumper guards are all rubber.

OPTIONS:

sunroof, tinted windshield, enamel porsche crest on wheels, chrome plated steel wheels, gasoline

heater (standard on S-models) (LHD models only), ambient temperature gauge, driver's side vanity

mirror on sun visor, recaro or ferrari seats (actually, both are made by recaro) leather seats,

headrests

1967 2.0 liter

Only 4 prototypes and 19 'production' 911Rs were made.

RECOGNITION TIPS:

The window cranks on 1967 cars are of the covered A-frame type but had a hard plastic knob. US

Models have chrome vertical bumper guards with a rubber strip (standard) -- 911S bumper guards

are all rubber. The bases for the switches on the dash go from black to chrome and the dash is

matte black (S model had basket weave vinyl).

OPTIONS:

Rear window wiper optional from this model year on (on Targas, too?), tinted windshield,

rear-window defroster (vertical wires), sunroof, sportomatic (introduced in 1967), enamel porsche

crest on steel wheels, chrome plated steel wheels, Fuchs alloys on non-S models, 100 liter fuel tank,

gasoline heater (standard on S-models) (LHD models only), ambient temperature gauge, leather

covered steering wheel (standard on S-models), driver's side vanity mirror on sun visor, leather

seats, headrests, recaro sport seats (available in leather, vinyl, vinyl with with corduroy, or vinyl with

hound's tooth inserts).

Early Power 1968-1973

Side marker reflectors appear in 1968 (tacked-on side reflector) -- in 1969 and later, the reflectors

are incorporated into the turn indicators. 1968 and later 911s have the model designation mounted

horizontally centered on the engine cover (the hood?). The covered headlight is replaced with a rim

bezel over a sealed beam headlight (US) or a lens covering bulbs (non-US). Inside, the window

cranks are one-piece with a soft vinyl knob. The door pockets under the arm rests are

vinyl-covered hard cardboard. 1969 is the first year of long wheelbase 911s; these came with flared

fender arches; also, the targas come with glass rear windows. The 911s between 1969 and 1973

used a 2 battery system. From 1970 on, the doors opened via trigger-type door handles. The

under-dash knee guard is a two-piece (with room for the ash tray in between) unit during this time

period. 1969 and later, the rear-view mirror is mounted to the windshield.

1968 (A Model) 2.0 Liter

A very few targas had glass rear windows at the end of the model year.

RECOGNITION TIPS:

Matte black wiper arms. US Models have chrome vertical bumper guards with a rubber strip

(standard) -- 911S bumper guards are all rubber. S Models have chrome vertical bumper guards

with a rubber strip. Knobs on the dash are now rubber covered. 1968 US models only, 911s had

tacked-on rectangular side reflectors in front and back. Two-piece dash pad (1968 only). Matte

black dash (S and L models had basket weave or elephant hide vinyl). Rear-view mirror is

break-away and ceiling-mounted.

OPTIONS:

sunroof, Sportomatic transmission (1968-1971), tinted windshield, rear- window defroster (vertical

wires), a chrome bar (optionally with leather rubber covering), connecting the top of the rear vertical

bumper guards (where bumper guards exist), a 3-piece stainless steel muffler skirt (hanging below

the rear of the car), enamel porsche crest on steel wheels, chrome plated steel wheels, Fuchs alloys

on non-S models, 100 liter fuel tank, gasoline heater (LHD models only), ambient temperature

gauge, leather covered steering wheel (standard on S-models), leather seats, headrests, recaro

sport seats (available in leather, vinyl, vinyl with corduroy, or vinyl with hound's tooth inserts) are

available on non-US cars.

1969 (B Model) 2.0 Liter

All new forced air ventillation system. Heated rear window standard. Targa had glass rear window.

911T came in an normal and 'Lux' configurations. 911T has all chrome bumper guards (rubber strip

is an option); 911E and S have all rubber bumper guards. After 1968, side marker reflectors were

incorporated into the turn-signal indicator.

RECOGNITION TIPS:

First year of long wheelbase 911s; these came with flared fender arches. Dash was basket weave

vinyl (1969-1971). If it's a LWB car with push- button outside door handles, it's a 1969.

OPTIONS:

Hydropneumatic struts on S model, Hella 169 fog lights (not available in US), sunroof, tinted

windshield, Sportomatic transmission (1968-1971), aluminum wheel arch mouldings (E and S

models), sportomatic, 5 speed (T and E models), rear-window defroster (horizontal wires), a

chrome bar (optionally with leather rubber covering), connecting the top of the rear vertical bumper

guards (where bumper guards exist), a 3-piece stainless steel muffler skirt (hanging below the rear

of the car), 10-spoke cast magnesium wheel (on T model only), chrome plated steel wheels, 100

liter gas tank (non-US models only), gasoline heater (LHD models only), electric antenna, leather

seats, headrests, vinyl and leather door coverings, vinyl or leather (or cloth?) sport seats, electric

windows

1970 (C Model) 2.2 Liter

Underfloor areas galvanized with PVC undercoat. 911T has all chrome bumper guards (rubber strip

is an option); 911E and S have all rubber bumper guards.

RECOGNITION TIPS:

First year of trigger-type door handles. '2.2' sticker in the back window. Dash was basket weave

vinyl (1969-1971). 1967-1970 glove boxes used a key lock which was mounted over the glove

box, but offset toward the center of the car.

OPTIONS:

Hella 169 fog lights (not available in US), Limited slip differential optional, sunroof, Sportomatic

transmission (1968-1971), tinted windshield, aluminum wheel arch mouldings (E and S models),

rear-window defroster (horizontal wires), a chrome bar (optionally with leather rubber covering)

connecting the top of the rear vertical bumper guards (where bumper guards exist), a 3-piece

stainless steel muffler skirt (hanging below the rear of the car), 10-spoke cast magnesium wheel (on

T model only), chrome plated steel wheels, 100 liter gas tank (non-US models only), gasoline

heater (LHD models only), Bosch hydro-dynamic struts (on T and S models only), electric antenna,

leather seats, headrests, vinyl and leather door coverings, vinyl or leather (or cloth?) sport seats,

electric windows

1971 2.2 liter

911T has all chrome bumper guards (rubber strip is an option); 911E and S have all rubber bumper

guards.

RECOGNITION TIPS:

Dash was basket weave vinyl (1969-1971). In 1971, the glove box lock was mounted in a twist

knob that appeared centered over the glove box.

OPTIONS:

Hella 169 fog lights (not available in US), tinted windshield, Sportomatic transmission (1968-1971),

heated windshield (this year only), sunroof, aluminum wheel arch mouldings (E and S models),

rear-window defroster (horizontal wires), a 3-piece stainless steel muffler skirt (hanging below the

rear of the car), 10-spoke cast magnesium wheel (on T model only), chrome plated steel wheels,

gasoline heater (LHD models only), electric antenna, leather seats, headrests, vinyl and leather door

coverings, vinyl or leather (or cloth?) sport seats (standard on S model), electric windows.

1972 2.4 liter

Stroked to get 2.4 liters; compression lowered to run on regular gas. Dry oil sump made of stainless

steel. The 901 transmission was replaced, starting in 1972, with the stronger 915 transmission. One

result of this is that these cars now use the conventional H shift pattern (drat!). Silver painted slotted

steel wheels standard on T model. Seat belts retract in US.

RECOGNITION TIPS:

Matte black engine grille, PORSCHE letters, seat recliner bars, and (on targa models) targa script.

1972-only had oil filler flap below right-side C-pillar. '2.4' badge on engine grille. Rectangular side

mirrors. Dash was leather grain vinyl (1972-1973) with no model designation.

OPTIONS:

Front spoiler optional, Sportomatic on E and T models, 5 speed on all cars in US and on T models

in UK, Larger fuel tank (with space saver spare), 6Jx15 alloys, Hella 169 fog lights (not available in

US or on E or S), tinted windshield, aluminum wheel arch mouldings (all models), rear-window

defroster (horizontal wires), sunroof, a 3-piece stainless steel muffler skirt (hanging below the rear of

the car), 10-spoke cast magnesium wheel (on T model only), gasoline heater (LHD models only),

electric antenna, leather seats, headrests, vinyl or leather door coverings, vinyl or leather (or cloth?)

sport seats, electric windows

1973

Better oil cooler, stronger main bearings. Large fuel tank standard (electric compressor provided for

the little-bitty tire that fits around the fuel tank). Front air dam standard on all models. 911 T and E

available in standard and Lux versions. Targa available mid-year in UK. Silver painted slotted steel

wheels standard on T model. E model used cookie-cutter wheels as standard. Seat belts retract in

US. This year only, Porsche produced the 2.7 liter Carrera RennSport or Carrera RS -- this was

available in four versions. The RS Sport and the RS Touring (RST) were the main customer

Carreras. Moreover, the many of the early RSs were made in lightweight form making them extra

fast (and extremely valuable). More esoteric RSs were the twenty RSH, or Homologation, models

and the 2.8 liter RS Racer (RSR).

RECOGNITION TIPS:

Matte black engine and horn grille, PORSCHE letters, and (on targa models) targa script. Bumper

guards on US models are made entirely of rubber. Rectangular side mirrors. Carrera had 'ducktail'

rear wing. Dash was leather grain vinyl (1972-1973) with no model designation.

OPTIONS:

Fuchs alloys on T model, Hella 169 fog lights (not available in US or on E or S), sunroof, tinted

windshield, aluminum wheel arch mouldings (all models except Carrera), rear-window defroster

(horizontal wires), a 3-piece stainless steel muffler skirt (hanging below the rear of the car), gasoline

heater (LHD models only), leather seats, headrests

Middle Years 1974-1977

Shock absorber bumpers, seats have fixed headrest. Along with the fat bumpers, the trunk (front of

the car) goes from curved-over to flat where it hits the bumper. The main-line cars all have 2.7 liter

displacements with CIS fuel injection.

1974 (G Model) 2.7 liter

Carrera available only in Coupe and Targa versions (no Sport, Touring, or Racing versions).

RECOGNITION TIPS:

Carrera 2.7 had 'ducktail' rear spoiler (but shock absorber bumpers). The bumper guards on

US-model 1974 cars were only about 3.5 inches wide. Newer cars have 7 inch wide bumper

guards. Note that the 1974 cars do *NOT* have thermal reactors (non-US cars never had them);

these things generate a lot of heat and, therefore, heat-related problems.

OPTIONS:

5-speed transmission (US -- this was standard in UK) or 4-speed Sportomatic

1975 2.7 liter

There was a silver anniversary edition of the 911 with silver cloth in seats and doors and black

leather trim.

RECOGNITION TIPS:

Black targa roll bar.

1976 2.7 liter

Carrera comes in regular and sport trim. Entire body covered in zinc for rust protection. 5-bladed

engine fan (rather than 11). Five speed transmission standard in US and UK.

RECOGNITION TIPS:

External mirror painted body color. Headlight washer is of the stick-up variety between 1976 and

1979.

OPTIONS:

sportomatic transmission, Koni adjustable or Bilstein gas/oil shocks (S Model), external oil cooler,

forged alloy wheels, sport seats, electric sunroof, electric windows, air conditioning

1977

Cars fitted with extra air pump, twin thermal reactors and exhaust recirculation. Improved gear box.

RECOGNITION TIPS:

Headlight washer is of the stick-up variety between 1976 and 1979.

OPTIONS:

sportomatic transmission, 5-speed transmission, center console

911SC and Later 1978 on

The fenders were flaired more dramatically from 1978-on. The rear badge of the 1978-1983 cars

had, of course, the '911SC' designation. Between 1984 and 1988, the badge on the engine lid

indicated the then-current model name, "Carrera". From 1980-on, the headlight washers were

mounted flush with the front bumper. The cabriolet body type was offered for the first time in 1983.

1978

5-speed standard. SC comes in standard and sport configurations.

RECOGNITION TIPS:

Headlight washer is of the stick-up variety between 1976 and 1979.

OPTIONS:

air conditioning, power windows, last year of the Sportomatic transmission

1979

SC horsepower increased mid-model year to 188.

RECOGNITION TIPS:

SC now has black window frames, electric windows. Headlight washer is of the stick-up variety

between 1976 and 1979.

OPTIONS:

air conditioning

1980

SC now has air conditioning and electric windows standard. The 911SC Weissach edition was

available in 1980. Flush-mount headlight washers start in 1980.

1981

SC was given a higher compression ratio for 1981. The SC still comes in standard and sports

configurations.

RECOGNITION TIPS:

Indicator side marking lights.

OPTIONS:

sports seats, berber cloth upholstery, leather upholstery

1982

1983

The Cabriolet was offered for the first time in 1983. This is the last year of the 911SC.

1984

RECOGNITION TIPS:

The easiest key is that the post 1983 cars had the name 'Carrera' on the engine lid rather than '911

SC'. These cars used the 'old' non-electric seats. Fog lamps in front spoiler.

OPTIONS:

air conditioning

1985

RECOGNITION TIPS:

First year of the electric driver-side seat.

OPTIONS:

Electric passenger-side seat.

1986

More effective air flow due to redesign of the ventilation system.

1987

New transmission with a hydraulic clutch is standard.

RECOGNITION TIPS:

The black "PORSCHE" script on the rear reflector is dropped this year in favor of clear script.

Halogen headlights (rather than sealed beam) are now fitted on US cars.

1988

959 available in sport and comfort trim. 911 Speedster . . 217n 195n . .

OPTIONS:

limited-slip differential (possibly turbo only), 16 inch wheels (possibly carrera only), alarm system

(possibly carrera only), 7" wide front tires (carrera only), 8" wide rear tires (carrera only)

1989

RECOGNITION TIPS:

Aside from the "Carrera 4" script on the back of the engine lid (the Carrera 2 came by in 1990), this

is the first year of the new smooth, body- colored bumpers. This is also the first year for standard

dual airbags and ABS.

1990

OPTIONS:

electrically adjustable seats

1991-1993

1994 993 (first year for ROW)

RECOGNITION TIPS:

This is the first year of the 993. This car stands-out with sloped headlights, a larger engine

cover/movable rear wing, and a handle- like fixed wing (with integrated third brake light) over the

back engine cover.

OPTIONS:

Available in Speedster configuration.

1995 993 (first year USA)

OPTIONS:

Tiptronic

Q1.4. But, Porsches are known for

performance; how do the models differ in

performance?<- ->

Check this out.

Note: 0-60 times are subject to the talents (and the desire not to damage the car)

of the driver. For this reason, the times will vary from source to source. This

table has used several different sources (some of which do not match). Don't

take the 0-60 times too seriously.

Table 1.  911 Models by Year and Type

--+--------------+------+----+-------+----+---+----+--------------+-----------

|              |induc-|0 to| Horse |    |top|    |              |

Yr| Model/Disp   |tion  | 60 | power |trq |spd| wt |    price     |

--+--------------+------+----+-------+----+---+----+--------------+-----------

64 911  2.0       Solex  8.3  130     120  130 2380

65 911  2.0       Solex  8.3  130     128  130 2380  2.5  7.9 16.0

66 911  2.0       carb   8.3  130     128  130 2207  2.5  7.9 16.0

66 911S 2.0       carb   8.0  160     132  140 2207  4.0 10.2 18.5

67 911  2.0       Weber  8.3  130     128  130 .     2.5  7.9 16

67 911S 2.0       Weber  8.0  160     132  140 2314  4.0 10.2 18.5

67 911R 2.0       Weber  .    210     .    .   1810

68 911  2.0       .      8.3  130     128  130 2207  3.7  6.2 10.0

68 911T 2.0       Weber  .    110     113  124 2185  4.5  6.4  8.1

68 911L 2.0       .      10.6 130     128  131 2314  5.3  8.8 12.5

68 911E 2.0       MFI    8.4  130     128  131 2185

68 911S 2.0 (q)   MFI    8.0  160     131  140 2132  4.0 10.2 18.5

69 911T 2.0       Weber  10.2 110     116  125 2250  3.5  7.8 16.0

69 911E 2.0       MFI    8.4  140     129  134 .     6.5 10.2 15.5

69 911S 2.0       MFI    8.0  170     134  170 2250  4.7  7.6 11.0

70 911T 2.2       carb   9.5x 125     130  127 2250  3.5  7.9 16.0

70 911E 2.2       MFI    7.6  155     141  137 .     6.0  9.0 15.0

70 911S 2.2       MFI    7.0x 180     147  138 2250  4.0 10.4 19.5

71 911T 2.2       (r)    9.5x 125     130  127 .     3.5  7.9 16.0

71 911E 2.2       MFI    7.6  155     141  137 .     6.0  9.0 15.0

71 911S 2.2       MFI    7.0x 180     147  138 .     4.0 10.4 19.5

71 911 racing     MFI    .    270     .    .   .

72 911T    2.4    (a)    9.5  130u    145u 127 .     3.0  9.1 24.5

72 911E    2.4    MFI    7.9x 165     152  138 .     4.0  9.8 22.0

72 911S    2.4    MFI    6.6x 190     159  144 .     6.2 17.6 28.5

72 911RSR  2.8    MFI    .    275-308 .    .   .

73 911T    2.4    (b)    9.5  130u    148  127 2250  3.0  9.1 24.5

73 911E    2.4    MFI    7.9x 165     152  138 2303  4.0  9.8 22.0

73 911S    2.4    MFI    6.6x 190     159  144 2303  6.2 17.6 28.5

73 Carrera 2.7 RS MFI    5.8x 210     187  143 2145 59.0 71.1 88.5

73 RSR     2.8    MFI    .    308     .    .   2145

73 RSR     3.0    MFI    .    315-330 .    .   .

--+--------------+------+----+-------+----+---+----+--------------+-----------

|              |induc-|0 to| Horse |    |top|    |              |

Yr| Model/Disp   |tion  | 60 | power |trq |spd| wt |    price     |

--+--------------+------+----+-------+----+---+----+--------------+-----------

74 911       2.7  K-Jet  7.9  150     175  130 2303  4.8 11.1 19.9

74 911S      2.7  K-Jet  6.1  175     175  140 2303  4.4 10.7 20.0

74 Carrera   2.7  (c)    8.5  175c    175c 131 2303 10.0 17.7 49.5

74 RS        3.0  .      .    230     201  .   .

74 RSR uk    3.0  .      .    315-330 .    .   .

74 RSR Turbo 2.1  .      .    480     .    .   .

75 911       2.7  K-Jet  7.9  150     175  130 2303  4.8 11.1 19.9

75 911S      2.7  K-Jet  6.1  160d    166d 140 2303  4.4 10.7 20.0

75 Carrera   2.7  K-Jet  8.5  165e    166e 131 2303  8.5 16.1 22.9

75 930       3.0  .      5.8  260     253  152 .

76 911       2.7  k-jet  7.2  165     175  135 .     4.8 11.1 19.9

76 911N (q)       .      .    .       .    .   .

76 911S      2.7  k-jet  7.5A 165     175  144A 2470 4.4 10.7 20.0

76 Carrera   3.0  k-jet  6.1  200     188  140 .

76 930       3.0  .      5.8  245g    253  152 2630 16.5 20.4 29.6

76 934       3.0  (f)    .    485-540 .    200 2464

76 935       2.8  .      .    580     .    .   .

77 911       2.7  .      7.2  165     175  135 .     4.8 11.1 19.9

77 911S      2.7  .      7.5A 165     175  144A.     4.4 10.7 20.0

77 Carrera   3.0  .      6.1  200     188  140 .    12.0 13.7 15.9

77 930       3.0  .      5.8  245g    253  152 .    15.5 23.2 30.0

77 934            .      .    .       .    .   .

77 935       2.8  .      .    370-590 .    .   .

78 911SC 3.0      k-jet  7.0  180     175v 140 2560  8.5 13.5 23.5

78 930   3.3      .      5.6  265h    291h 155 .    16.9 22.3 29.5

78 935   2.86-3.2 .      .    590-900 .    227 2255

78 936   2.1      MFI    .    580     .    .   .

79 911SC 3.0      k-jet  7.0  180     175v 140 2560  8.0 13.9 20.0

79 930   3.3      .      5.6  265h    291h 155 2870 18.5 26.5 42.5

79 935            .      .    .       .    .   .

79 936   2.1      MFI    .    580     .    .   .

80 911SC 3.0      k-jet  7.0x 180     180v 140 2760  8.5 14.7 27.5

80 930   3.3      .      .    (j)     304  .   .    21.9 23.4 24.9

80 935   3.2      .      .    740     .    .   .

81 911SC 3.0      k-jet  7.0  180t    180t 140 2760  8.7 15.8 24.0

81 930   3.3      .      .    (j)     304  .   2860 19.3 24.5 27.8

81 935   3.2      .      .    760     .    .   .

81 936   2.7      MFI    .    600     .    .   .

82 911SC 3.0      k-jet  7.0  180t    180t 140 2760 10.0 16.5 23.0

82 930   3.3      .      .    (j)     304  .   2860 18.9 27.2 37.5

82 956   2.7      MFI    .    620     .    .   .

83 911SC     3.0  k-jet  7.0  180t    180t 140 2760 10.0 17.1 30.0

83 930       3.3  .      .    (j)     304  .   2860 21.0 27.6 33.0

83 911 SC RS 3.0  .      .    255     .    .   .

83 956       2.7  d-mot  .    620     .    .   .

--+--------------+------+----+-------+----+---+----+--------------+-----------

|              |induc-|0 to| Horse |    |top|    |              |

Yr| Model/Disp   |tion  | 60 | power |trq |spd| wt |    price     |

--+--------------+------+----+-------+----+---+----+--------------+-----------

84 Carrera 3.2    mot    5.6  207k    192k 149 2760 21.0 25.2 30.0

84 930 3.3 (q)    .      .    300     .    .   2860 22.5 30.5 43.5

84 911 SC RS      .      5.0  .       .    159 .

84 962 2.8        .      .    650     .    .   .

85 Carrera 3.2    mot    5.6  207k    192k 149 2760 14.5 21.3 36.5

85 930 3.3 (q)    .      .    300     .    .   2860 26.0 31.7 39.9

85 959            .      .    .       .    .   .

85 962 3.2        .      .    700     .    .   .

86 Carrera 3.2    mot    5.3  207k    192k 149 2760 14.3 22.5 34.0

86 930 3.3        .      .    282m    287  .   .    24.5 34.2 34.2

86 959            .      .    .       .    .   .

86 961            .      .    .       .    .   .

87 Carrera 3.2    mot    5.3  217n    195n 149 2670 16.9 25.5 45.9

87 930 3.3        .      5.4  286p    287  162 2940 27.0 36.6 48.9

87 959            .      .    .       .    .   .

88 Carrera 3.2    LE-jet 5.3  217n    195n 149 2770 17.5 26.6 40.0

88 911 Club Sport .      5.3  217n    195n 154 2550

88 911 Turbo      k-jet  5.0  282w    289w 155 3055 28.9 43.1 64.9

88 959 Sport 2.9  .      .    450     .    197 .

89 Carrera  3.2   .      5.3  217n    195n 149 .    25.9 30.5 40.0

89 911 Club Sport .      5.3  217n    195n 154 2550

89 964 (C4) 3.6   .      .    250     229  .   .    29.0 34.9 43.5

89 911 Turbo      k-jet  5.0  282w    289w 155 3055 39.0 50.9 65.0

90 964 (C2) 3.6   .      5.7  250     229  161 3031 28.0 35.9 52.0

90 964 (C4) 3.6   .      5.8  250     229  161 3320 30.0 37.7 50.0

90 Turbo    3.3   .      5.1  300     .    159 3055

91 964 (C2) 3.6   .      5.7  250     229  161 .    32.0 41.0 55.0

91 964 (C4) 3.6   .      5.8  250     229  161 3197 37.9 43.5 53.0

91 C2 Turbo       .      5.0  320     .    168 3274 51.9 60.7 69.0

92 964 (C2) 3.6   .      5.7  250     229  161 3197 38.0 45.0 53.0

92 964 (C4) 3.6   .      5.8  250     229  161 .    43.0 46.8 55.8

92 RS America     .      .    250     229  .   .

92 962 (C2) RS    .      .    260     240  .   .

92 Turbo          .      5.0  320     332  168 .    58.7 70.8 85.0

92 Turbo S        .      4.6  381     361  180 .

93 964 (C2) 3.6   .      5.7  250     229  161 .    43.0 49.9 61.5

93 964 (C4) 3.6   .      5.8  250     229  161 .    48.9 51.9 55.0

93 RS America     .      .    250     229  .   .    38.5 43.3 51.5

93 C2 Turbo       .      4.8  360     384  175 .

94 993 (s)        .      5.4  .       .    168 .

94 930 3.6        .      .    .       .    .   .    84.9 90.0 98.5

95 993 (C2)       .      5.3  270     .    168 3065 53.7 61.0 69.3

95 993 (C4)       .      .    270     .    .   3065

--+--------------+------+----+-------+----+---+----+--------------+-----------

|              |induc-|0 to| Horse |    |top|    |              |

Yr| Model/Disp   |tion  | 60 | power |trq |spd| wt |    price     |

--+--------------+------+----+-------+----+---+----+--------------+-----------

--------------------------

Key:

carbureted (multiple or unknown types)

Zen              Zenith 40TIN Carburetors

Web              Weber 40 IDT Carburetors

Sol              Solex 40 PI Carburetors

MFI              Bosch Mechanical fuel injection

k-jet            Bosch K Jetronic fuel injection (same as CIS)

mot              Bosch Motronic fuel injection

Model/Disp       Model / Displacement (in Liters)

0 to 60          0 to 60 MPH in Seconds

Horsepower       Horsepower (DIN)

trq              Torque in Pounds Feet

top spd          Top speed in Miles per hour

weight           Weight in Pounds

price            1995 asking prices in thousand US dollars (rounded off)

taken from July 1995 and January 1995 issues of the

Porsche Market Letter (thanks Phil!).  Note: speedsters

and cabrios were prices separately and will cost more

than the prices shown.

Notes:

a  US models have MFI (w/140 HP); UK models have Solex or Zenith

Carbs (w/130 HP)

b  Early models have MFI, 73 1/2 models have CIS.

c  210 HP, 188 lb. ft. Torque in ROW, UK models have mfi; US models

have ?

d  49-state us models have 165 HP, California has 160, ROW has 175 HP;

ROW has 175 lb. ft. of Torque.

e  210 HP, 188 lb. ft. of Torque for ROW

f  k-jet (non-us) or mech (us)

g  245 HP in US & Japan; 260 HP elsewhere

h  265 HP in US and Japan, 300 HP elsewhere; 304 lb. ft. in ROW

j  Not available in US, 265 HP in Japan, 300 HP elsewhere

k  207 HP in US and Japan, 231 HP elsewhere; 192 lb. ft. in US and

Japan, 209 lb. ft. elsewhere.

m  282 HP in US, 300 HP in ROW; 195 lb. ft. in US, 209 lb. ft. in

ROW

n  217 HP in US, 231 HP in ROW

p  286 HP in US, 300 HP in ROW

q  European Model

r  Weber/Zenith

s  Rest Of World Model

t  180 HP in US and Japan, 204 HP elsewhere; 195 lb. ft. Torque

in ROW

u  140 HP, 148 lb. ft. Torque in ROW

v  195 lb. ft. Torque in ROW

w  282 HP in US, 300 in ROW; 287 lb. ft. Torque in US, 319 lb. ft.

in ROW

x  Time is a 0-62 MPH (0-100 KPH)

A  0-60 is 7.5 seconds for US version, 6.1 for ROW.  Top speed is

144 MPH for US version 142 for ROW.

Q1.5. What should the VIN or engine

number look like for my car? <- ->

Well, I'm not going to go into that here 'cause it's long and there are so many other books that do it

completely. For VINs, check out Bruce Anderson's "Porsche 911 Performance Handbook" or

"Guide to Purchase & DIY Restoration of the Porsche 911". For both VINs and engine numbers,

consult Brett Johnson's Restorer's guides or "The Used 911 Story" (for US cars only).

Q1.6. Why did the early 911s have two

batteries? <- ->

As per Pete Albrecht:

Very early cars also had cast iron (NOT LEAD!) weights in the outer corners of the

front bumpers for the same reason.

[Tobias] Aichele's book, ["Porsche 911: Forever Young", Beeman Jorgensen, 1995]

recounts the tests run with various configurations (originally lead weights for testing

only). In tests supervised by Helmuth Bott, with the weights in the outer corners of the

bumpers, the steering had an appreciably higher self-centering moment. Moving the

weights to the center of the bumpers worsened the handling characteristics again. "The

inescapable conclusion was that the handling problem was not only caused by the

weight distribution, but was also sensitive to the car's polar moment of inertia. Helmuth

Bott draws an analogy: 'These laws of physics are even used by ice skaters, when they

spread their arms to slow their rotation or pull them in to turn faster.'"...

"Bott took a front bumper to the Bodenmueller foundry, located across the street from

Porsche, and had sand molds of the bumper tips made. These molds provided iron

castings weighing 24 lbs which were cemented into the bumpers with a particularly

tough adhesive and also clamped by the bumper's mounts." ..."Helmuth Bott recalls

that "We didn't want to publicize this solution with its reinforced bumpers, but we were

happy to have found a bolt-on remedy."

The bumper weight idea is an extension of the idea of mounting the batteries as far

toward the corners of the car as possible.

Peter Albrecht, PLAlbrecht@aol.com, "Why twin batteries",

951019125859_48727898@mail06.mail.aol.com

On the other hand, Derek Cahill suggests:

[...] There is a LARGE amount of oil in a 911 engine, and in order to get it moving on

a cold morning, using the best technology of 1967, two batteries were needed (there

was no such thing as a battery with 800 CCA's readily available back then, so two

400-450's did the same job) to provide the necessary power to start the car.

Derek Cahill,"Re: Twin Batteries why",

Pine.3.89.9510192013.A27106-0100000@freenet3.scri.fsu.edu

Q2.1. Which 911 Should I Get? <- ->

The standard answer is "get the newest 911 you can afford". Unfortunately, it's more complicated

than that. I had occasion to meet Joe Rusz, Senior Editor at Road & Track (gratuitous name

dropping, here); his answer to this question was simply "if you can afford it, get one with Motronic

Fuel Injection" (those'd be the ones built in 84 and after).

You really have to decide for yourself what you want. Many feel that one exception to the 'newest

you can afford' rule is the middle year cars (1974 through 1977) due to their short engine life span

(circa 50K miles). Others (like myself) prefer the early mechanically injected cars (light and sparcely

appointed with quick, torquey engines) over the newer 911SC (with their air conditioning, electric

windows, and bullet-proof engine).

Hopefully, the information in this document will help you decide.

Q2.2. I want to buy a 911. How should I go

about it? <- ->

There's lots of stuff.

DECIDE WHY YOU WANT THE CAR. Decide whether you want an old show car, a race car,

a daily driver, or whatever. This should help you settle on which types of 911 are best for you.

HOMEWORK. Get some books and research the different cars (check out the references at the

end of this FAQ). When it comes to information, some is good, more is better, and too much is just

enough. Figure out which years, models, and features of 911 are in your list.

Once you decide on a car type, find out what can go wrong with them and how much it can cost to

fix them.

PRICES. Check out the usual sources for prices and availability:

The Porsche Market Letter, (619) 727-4856, 1 yr subscription $55

Panorama (the newsletter to the Porsche Club of America),

The Auto Trader, (800) 845-9612. Some regions also have the Sports Car Trader.

Hemmings Motor News, (800) CAR-HERE

The Recycler,

The local newspaper,

The Penny Saver,

Porsche Swap Meets.

Shop for insurance at this point. You don't want to find your dream car and find out you can't afford

to insure it. Insurance companies vary drastically (as do the costs for the different years and

models).

CHECK OUT FINANCING. If you want an older 911, you may have some trouble getting a

loan. Used car loans usually only apply to cars with a value listed in the Kelly Blue Book (those that

deal with older cars usually do so based on a rediculously low estimate of the value of the car). If

you don't have extra dollars hanging around, you may have to get an unsecured loan (at a higher

interest rate).

FIND A MECHANIC. Especially if you are able to look for a car close-to-home, find a mechanic

before you start looking. Ask friends who their mechanics are and talk to PCA and POC personnel.

Talk to your mechanic (and other knowledgeable people) about what you should be looking for in a

car.

LOOK FOR A CAR. Now that you know the car (and price range) for which you are looking,

start your search. Take lots of information including VIN, etc.

CHECK-OUT THE CAR. If the car is long distance, you may have the owner take it to a

mechanic first. I tend to like to use Porsche dealers for long distance check-outs. Dealers may be

more expensive but they should know their stuff.

If the car is nearby, check-out the car in person first. Look for features, rust, and general condition.

Test drive your car: does it start easily, does it accelerate with no flat spots, does it go into all gears

easily? After the car has been warmed-up, ask the owner and take it to redline. If he resists, ask

him to do so. Make sure the car revs freely and that there's no smoke when you do this.

TAKE THE CAR TO A MECHANIC. Have the mechanic do a compression check and a

leakdown. Have him make sure the engine numbers match the VIN. He should be able to itemize

everything you need to put the car into street concourse condition (even if you don't want to show

the car, this will give you an idea of everything the car needs). The list should help you decide

whether you want this car and, if so, the price range for the car.

CHECKLIST. Check out the following checklist for some ideas of stuff for which to look.

BUY THE CAR. Join the PCA / POC. Enjoy your car.

Q2.3. Does anyone have a checklist for

potential 911 buyers? <- ->

Here it is. . .

NAME/ADDRESS/PHONE

.                                     Car _________________________________

.

.                                     Price _______________________________

.

DATE:

== PHONE =====================================================================

VIN ____________________

Miles ___________________________

How Long Owned __________________     How Many Owners ____________________

Records _________________________     Where maintained ___________________

Color ___________________________     Last Paint Job _____________________

Interior Color___________________

Wheel sizes _________    Tire sizes _________     [ ]  Original Color

[ ]  Original Engine     [ ]  5 speed manual      Induction ____________

[ ]  Air Conditioning    [ ]  Alarm               Radio ________________

[ ]  Large Fuel Tank     [ ]  Gasoline Heater

[ ]  Electric Windows    [ ]  Electric Antenna

Why Selling, Notes:

== RECEIPTS ==================================================================

[ ]  Carrera Tens'ners   Last Overhaul ____________

[ ]  Rebuilt Inj'n pump (mfi)

[ ]  Shuffle Pin (f)     [ ]  RaceWare Studs (f)   [ ]  Timeserts (f)

Compression 1:____ 2:____ 3:____ 4:____ 5:____ 6:____

== LONG DISTANCE =============================================================

Have the owner send receipts and pictures.

If you can, have the owner send a videotape.  The tape should

cover the following:

- Walk around the car, SLOWLY

- Get closes-up (check for rust & mating) of:

headlights, door seams (door closed), hood, trunk,

fuel filler,

- Get under-car shots including:

suspension pickups (front and rear), jack receiver area, and

tortion bar tubes (under car).

- Interior shots (take-off targa top, if applicable).  Get:

front seat, rear seat, dash, instruments, console (if

applicable) carpeting

- Engine compartment

- Trunk area (lift carpet around batteries).

Have owner take the car to a mechanic.

Maybe have owner take the car to a body shop (check for rust).

Check seams for evenness and for rust (portal closed)

[ ] left door            [ ] right door           [ ] fuel filler flap

[ ] hood (mating)        [ ] trunk

Check for rust (under car):

[ ] left jack receiver   [ ] right jack receiver

[ ] front suspension     [ ] rear suspension

[ ] headlights           [ ] tail lights          [ ] under windshield

[ ] trunk area (lift carpet around batteries)

Interior (take-off targa top, if applicable)

[ ] front seats          [ ] rear seats           [ ] dash

[ ] carpeting

(RECEIPTS, MECHANIC)

== INSPECTION (bring magnet, ice pick, flashlight) ===========================

Name ____________________  Phone ____________________  Car ___________________

GENERAL

A B C D F   Paint, chrome, trim    A B C D F   Rubber

A B C D F   Dents/Dings            A B C D F   Undercoat all around (e)

LEFT SIDE DOOR:     VIN Drivers door jamb (post '69) ____________________

A B C D F   Mating                 A B C D F   Edge, bottom (r)

A B C D F   Hinge                  A B C D F   Strike Plate (r)

A B C D F   Jack receiver (r)      A B C D F   Underside rocker panel (r)

A B C D F   Side windows & seals   A B C D F   Body under windshield (r)

TOP

A B C D F   Targa top seal         A B C D F   Targa top condition

LEFT FRONT FENDER: VIN Windshield post (post '69)    ____________________

A B C D F   Tire condition         A B C D F   Fender Lip Texture (a)

A B C D F   Fuel filler (r)

TRUNK: VIN (post '73)                                ____________________

A B C D F   Headlights (pull out, rust & bracket squareness)

A B C D F   Cross-member in front of gas tank (been beaten flat?)

A B C D F   Suspension pickups under car L&R (r)

A B C D F   trunk lid: fit (r)     A B C D F   trunk lid stop (r)

A B C D F   Battery Box (r)        A B C D F   Front bumper - fit

A B C D F   Spare tire             A B C D F   Jack and toolkit

RIGHT FRONT FENDER

A B C D F   Tire condition         A B C D F   Fender Lip Texture (a)

RIGHT SIDE DOOR

A B C D F   Mating                 A B C D F   Edge, bottom (r)

A B C D F   Hinge                  A B C D F   Strike Plate (r)

A B C D F   Jack receiver (r)      A B C D F   Underside rocker panel (r)

A B C D F   Side windows & seals   A B C D F   Body under windshield (r)

RIGHT REAR FENDER

A B C D F   Tire condition         A B C D F   Sight along body (accident)

A B C D F   Suspension Pickups (d) A B C D F   Texture on fender lip (a)

A B C D F   Pinch Welds (g)

ENGINE LID / COMPARTMENT: VIN Under hood (pre '74)   ____________________

Engine number (vertical fan housing)               ____________________

A B C D F   General condition      A B C D F   Belts

A B C D F   Oil leaks              A B C D F   Transmission fluid leaks

A B C D F   Exhaust system         A B C D F   Rear Valence (accident)

A B C D F   Tail & parking lights  A B C D F   Brake lights, signals

A B C D F   Backup lights          A B C D F   Seams/Fit (accident)

LEFT REAR FENDER

A B C D F   Tire condition         A B C D F   Sight along body (c)

A B C D F   Suspension Pickup (d)  A B C D F   Texture on fender lip (a)

A B C D F   Pinch Welds (g)

INTERIOR:

[ ]  Leather           [ ]  Sport seats         [ ]  Head Rests

A B C D F   Front Seats             A B C D F   Rear Seats

A B C D F   Carpeting               A B C D F   Floor pan/pedals (r)

A B C D F   Air Condonditioner      A B C D F   headliner

A B C D F   Dashboard               A B C D F   Seat adjustment (L&R)

== TEST DRIVE ================================================================

A B C D F   Starting     A B C D F  Acceleration  A B C D F   Braking

A B C D F   Alignment    A B C D F  Steering      2  3  4  5  Synchros

A B C D F   Clutch pedal free play    A B C D F   Brake Pedal Firmness

A B C D F   Clutch slippage           A B C D F   Idle (fluctuations)

A B C D F   Valve sounds              A B C D F   Clutch chatter

A B C D F   Other strange sounds      A B C D F   Blip throttle (miss=inj'n,

_________   Oil pressure (warm)                   smoke=valve guides)

== MECHANIC ==================================================================

Name ____________________  Phone ____________________  Car ________________

Mechanic ________________  Phone ____________________

Everything required to bring the car to street-concours, itemized and costed

1:____ 2:____ 3:____ 4:____ 5:____ 6:____ compression (130-170 +- 15%)

1:____ 2:____ 3:____ 4:____ 5:____ 6:____ leakdown (< 3-5%, 10% max)

[ ]  Numbers Match       [ ]  Engine number match [ ]  Worn Valve Guides

[ ]  Carrera Chain Tensioners         [ ]  Spring Centered Clutch (b)

A B C D F   Tie rod ends              A B C D F   CV joints

A B C D F   Ball Joints               A B C D F   Bushings

A B C D F   Shock absorbers/struts    A B C D F   Brake lines

A B C D F   Structural Rust           A B C D F   Cosmetic Rust

A B C D F   Front susp. attachment    A B C D F   Rear susp. attachment

A B C D F   Torsion bar tubes (F&R)   A B C D F   Lower control arms (F&R)

A B C D F   Floor pan-(F&R)           A B C D F   Floor pan-battery area

--------------------------------------------------------------------------

Resolution:

VINs / Engine No. Match

Rust

Accidents

Mechanical Condition

(a) since 1969

(b) 911SC only

(c) check for accident damage

(d) The rear suspention pickups are bolted to the pan under the car

roughly aligned with the torsion bar tubes -- check for rust.

(e) Fresh undercoat is bad.  If you see it, check to see what mischief

it covers.

(f) These are not required if the car isn't a 2.7 liter or heavily built-up car.

(g) Make sure the pinch welds aren't bulging or separating.

(r) check for rust

Q3.1. What are the classic problems/areas

to check on 911s?<- ->

The 911 is a really good car but there are a few problem areas that have, at various times, plagued

this particular vehicle.

First, the results of an on-going survey of 911 repairs is given in the tables below. The tables are

broken into Major (~$1000 and above), Not Quite So Major (less than $1000), Maintenance (ya

gotta plan to do these), and Optional (fun, but not necessary to keep the car on the road).

Major.

Repair

pre-69

69-73

74-77

78-83

84-89

90-93

93-

Unspecified

Brake Rotors ($800) .

1

Chain Tensioners ($1000)

1

Engine Overhaul ($5000)

1

Master Cylendar

1

1

Rust Repair ($var)

1

Not Quite So Major.

Repair

pre-69

69-73

74-77

78-83

84-89

90-93

93-

Unspecified

Alternator/Regulator ($240-$400) .

1

2

Battery ($123-$150)

2

1

Engine Oil Thermostat ($400)

1

Front Windshield ($450)

1

Fuel Pump ($250+labor)

1

Heat Exchangers

1

Hood/Engine Lid Shocks($111)

1

1

Muffler

1

New Clutch Lever & Cable ($200)

1

Small Misc (washers, cig lighter,

dash vent, speedo/tach overhaul)

1

3

1

Tie Rods ($160+labor)

1

Replace Window ($498)

1

Tortion Bracket ($100 ea.)

2

Trim Repair ($var)

1

Maintenance.

Repair

pre-69

69-73

74-77

78-83

84-89

90-93

93-

Unspecified

Airbag Service($48.75) .

1

Brake Pads/Flush

1

1

1

1

Major Service ($991)

2

1

1

Minor Service / Oil Change

($30-$166)

2

1

2

1

Shocks ($550)

1

1

Tires ($175-$200/tire)

1

1

Windshield Wiper Blades

1

1

Optional.

Repair

pre-69

69-73

74-77

78-83

84-89

90-93

93-

Unspecified

Rear Sway Bar ($600) .

1

Seats Recovering ($350-$425)

1

1

Some Detailed Information

Below is a list of some of the most notorious problems.

Rust

Rust can destroy a 911's unit-body and this can be really expensive (impossible?) to fix. Watch

closely for rust, particularly with the pre-galvanized bodies (pre-1976?). Check the seams around

and edges of the doors, trunk, and hood. Check the jack points and the torsion bar tubes.

Heat exchangers rust along with everything else. Be careful, this can lead to carbon monoxide

poisoning of your car's occupants. Many replace theirs (their exchangers, not their occupants) with

stainless steel once.

Chain Tensioners

The timing chain is held taught by chain tensioners. The early (pre-1984) timing chain tensioners

tended to wear out and suddenly collapse causing your pistons to come in violent contact with your

valves. This gets expensive. The 1984 and later cars used oil- fed tensioners which solved the

problem.

Many early 911 owners have had their older chain tensioners replaced with Carrera tensioners. This

modification requires about six hours of labor with parts costing around $300-$400 per bank of

cylendars (roughly $1000). Adding carrera tensioners is even more expensive on pre-1967 engines

because the updated parts don't fit correctly.

Some have modified their tensioners by adding mechanical tensioner guards. These devices keep

the tensioners from collapsing completely when they collapse. I have heard failure stories as well as

success stories regarding tensioner guards.

Worn Mechanical Fuel Injection Pump

The injection normally doesn't require too much adjustment. In around 100,000 miles, however, fuel

injection pumps wear out. A worn pump manifests itself usually by running too rich beyond the

control of adjustment. The pump usually costs between $800 and $1500 to be rebuilt.

Many people replace their worn mechanical injection with weber carburators but purists, like me,

hate to see this kind of thing happen. If you do change-out your injection, at least save it so a future

owner of your car can return it to original condition.

Exploding Clutch

The 911SC (1978-1983) used a rubber-centered clutch which would eventually fail and send

rubber pieces sailing throughout that part of the transmission. These clutches should be replaced by

a spring-centered one.

Exploding Airbox

The 2.7 and 3.0 liter 911 cars use a $200 airbox that can, if the car backfires while starting,

explode. For around $15, you can get a pop-off valve that is supposed to fix this problem.

Puff of Blue Smoke on Startup

This is not a problem. 911s tend to have oil seep into the cylendars when they sit at rest. When the

car is started, the oil burns and this gives you the puff of blue smoke. This is normal and does not, in

and of itself, require any fix.

Carrera 2/4 Distributors

There's an internal belt in the distributor of the Carrera 2 and Carrera 4 cars that breaks at about

50,000 miles. Unfortunately, the fix is a new distributor at a cost of somewhere around $1000.

Q3.2. So, what's all these problems I keep

hearing about the 2.7 liter 911s?<- ->

It's a tragic story. Porsche increased the displacement of the 2.4 without providing enough cooling

and, to add insult to injury, the US models had thermal reactors (except for 1974) that got

REALLY hot. The result is, among other things, head studs that pulled out of the crank case (due to

thermal expansion of the cylinders) and destroyed valve trains. All of this resulted in an average

engine life of about 50,000 miles (your mileage may vary -- HA! I was *waiting* to use that line).

So the natural follow-on question (so natural, in fact, that I'm not breaking it out into its own

question) is "can anything be done to mitigate the design flaws of the 2.7?" The answer is:

Have the case helicoiled or timeserted. These threaded inserts are installed in the crank case

to hold the cylinder studs tightly and keep them from pulling.

Use Raceware studs. These studs won't pull out because they expand with temperature at the

same rate as the cylendars. Dilivar studs used to be the choice for this repair, but several

people have had trouble with them breaking.

Replace the 5-blade fan with an 11-blade fan.

Add an extra oil cooler.

Carrera tensioners (of course).

Other people suggest replacing the 2.7 liter engine with a later-model 3.0 or 3.2 liter engine. The

cost of a (slightly) used 3.0 is about the same or even cheaper than rebuilding a 2.7.

Q3.3. Where can I get NEW and USED

stuff for my 911? <- ->

Currently, this is just a list of mail order houses. Hopefully, I'll get email with information to fill-in

some of the extra columns. That data will make this a much more useful guide.

Special thanks to Douglas Blondin, keeper of the Photographic Mail Order FAQ. I

stole the format for this section from him -- with his permission, of course.

DISCLAIMER: The figures presented here represent neither an endorsement or a condemnation of

any particular company. Rather, this table is simply a compilation of experiences sent in by various

netnews readers. Experiences are personal experiences and are NOT related to the company of the

editor nor of any company of a person who is relating an experience. Also, this is a non-scientific

survey, the chart may not reflect the reality of experiences for any given company. Your actual

ordering experience may differ, and companies may change over time.

USE OF THE SURVEY: This survey is maintained for the readers of the Internet to aid them in

choosing a company from which to order equipment. Companies may also use the survey to see

what some customers are saying about their company (or competitors). Any other use of the survey,

such as in advertising, is strictly prohibited. Questions about possible use of the survey should be

directed to the editor.

UPDATES/NEW EXPERIENCES/OTHER INPUT: Your easiest method is to send your

experiences at the e-mail address listed below. When sending input, please make sure that your

message contains the following information:

company name :: be careful in spelling et al; I don't know all companies, so may mistake a

misspelling for a new company name

categorization of experience (no problem, minor problem, major problem, avoid) :: I can't

read minds and do not like to try to infer from your other words; submittals that do NOT

contain a categorization run the likely fate of being unceremoniously left out of the survey

SURVEYS IN GENERAL: The consumer must take all input (magazine ratings, this survey, other

surveys, friend's advice, ...) and put whatever faith in them that they will. Companies may change

over time (both for better and worse), and different people/magazines may have different standards.

In the final analysis, you must make the decision and you're likely to have a unique experience from

anyone else.

The numerical summary of experiences reported by readers. They are split into 4 categories:

GREAT experience. Something about dealing with this company (e.g., the servie or the

price) was much better than expected.

No problems. Got what you ordered, in reasonable time, at expected price, no unpleasant

surprises.

Minor hassles. Minor delays, unpleasant saleperson, hard to get through to toll free line;

probably not enough to keep you from ordering from them again.

Major hassles. Major problems occurred, but you were satisfied enough with with the way

they were resolved that you might consider ordering from them again when you cool off.

Avoid. Major problems occurred that either were not satisfactorily corrected or that you feel

were significant enough to begin with that you wouldn't consider ordering from them again

under any circumstances.

Following are new and used parts houses.

Vendor

Phone

Address

GREAT

Experience

NO

Problem

MINOR

Hassles

MAJOR

Hassles

Avoid

Notes

Aase

Brothers

(800)

444-7444

(714)

956-2419

701 East

Cypress St

Anaheim, CA

92805

.

.

.

.

.

Used parts.

AJ-USA Inc

(800)

877-1911

(619)

452-8900

6620 Mira

Mesa

Boulevard

San Diego

CA

92121-4300

.

.

.

.

.

.

Andial

(714)

957-3900

3203-3207

South

Shannon

Street

Santa Ana,

CA 92704

.

.

.

.

.

.

Automotion

(800)

777-8881

(408)

736-9020

193P

Commercial

Street

Sunnyvale,

CA 94086

.

.

.

.

.

.

Best Deal

(800)

354-9202

(714)

995-0081

8171

Monroe

Avenue

Stanton CA

90680

.

.

.

.

.

Used parts.

Carlsen

Porsche

.

Palo Alto,

CA

1

.

.

.

.

.

Doc & Cy's

Restoration

Parts

(800)

950-0356

50 E. Morris

Street

Indianapolis,

Indiana

46225

.

.

.

.

.

Rubber and

other

reproduction

stuff.

Engine

Builders

Supply

.

.

1

.

.

.

.

.

German

Parts and

Restoration

(805)

549-8525

San Luis

Obispo, CA

.

.

.

.

.

.

Imparts

(800)

325-9043

8401 Hanley

Industrial

Court

St. Louis,

MO 63114

.

.

.

.

.

.

PartsHeaven

(800)

767-7250

(510)

782-0354

1680 West

Winton

Avenue,

Suite 4

Hayward,

CA 94545

2

.

.

.

.

Used parts.

Parts Shop

(800)

767-7250

(510)

782-0354

1680 West

Winton

Avenue,

Suite 4

Hayward,

CA 94545

2

.

.

.

.

New Old

Stock and

Reproduction

Parts.

Performance

Products

(800)

789-1960

(818)

787-7500

7658 Haskell

Avenue

Van Nuys,

CA 91406

.

.

.

.

.

.

Stoddard

(800)

342-1414

(216)

951-1040

38845

Mentor

Avenue

Willoughby,

Ohio 44094

.

.

.

.

.

.

Stuttgart

Haus of

Parts

(800)

356-4379

(704)

664-4708

150 Bypass

PO Box

1555

Mooresville,

NC 28115

.

.

.

.

.

Used parts.

V&P

Heaven

(800)

756-0956

(310)

927-5575

6393 East

Florence

Avenue

Bell Gardens,

CA 90201

.

.

.

.

.

Used parts.

90 day

guarantee.

Zims

Autotechnik

(800)

356-2964

(817)

267-4451

1804

Reliance

Parkway

Bedford,

Texas 76021

2

.

.

.

.

.

These are some general guidelines developed by readers over the years. As with any guideline,

there are times when it is appropriate to "break" them. However, as many survey users can attest, if

you don't follow one of the following there is a good chance that you'll be sorry.

ORDER BY CREDIT CARD ONLY. Don't pay the credit card bill until you have received

the goods in satisfactory condition. To avoid interest charges, when you pay the rest of the

credit card bill, include a note explaining the contested charge.

ASK WHAT THE SHIPPING AND HANDLING CHARGES WILL BE. Most stores no

longer just charge you the freight, but also include a sizable handling charge.

WHEN ORDERING, ASK FOR THE NAME OF THE SALESPERSON. Record this

piece of information along with the time, date, and agreed upon sales price and merchandise.

WHEN YOU GET YOUR EQUIPMENT, TEST IT IMMEDIATELY. If it is defective, call

the mail order company immediately and arrange for returning it. See #1 above. Ask for a

return authorization number and get the name of the person you talk to. Most stores give you

rather short period for returning defective equipment, so waste a roll of film and get it

developed at a one day service place.

ASK IF THE ITEM IS IN STOCK.

Q3.4. At what pressure and temperature

ranges should my 911 operate? <- ->

The sources I have checked largely agree with each other. My 2.4 Owner's Manual (it covers T, E,

and S models) states that the temperature should not exceed 265 F. According to an article by

Bruce Anderson. . .

Oil Temperature

Meaning

180-220 F

Normal operating temperature

230 F

Warm

240 F

Hot

250 F

Too Damn Hot

According to Pete Albrecht (<960627183812_423165721@emout17.mail.aol.com>),

"Our personal max temp while running 600 hour endurance runs on the dyna at

Porsche (for non-Porsche engines but that doesn't matter) was I think 130 deg C

which is 266 F. 120 C was more typical but it could get up to 130. Of course we

changed oil regularly. Modern oils can take more heat before breaking down than the

stuff 20 years ago. You really WANT the oil to get above 100C, 212 F, to get the

condensate water out of it."

Pete Albrecht, PLAlbrecht@aol.com, "Re: Oil temps, continues",

960627183812_423165721@emout17.mail.aol.com

On oil pressure, it should be between 10 and 15 pounds per thousand RPM. My Owner's Manual

states that pressure should not drop below 70PSI at 5500 RPM. Moreover, the oil level should

never drop below the minimum mark on the dip stick (remember to check the oil on level ground

while the engine is running and the temperature is over 180 F).

Q3.5. Where can I find a car seat for the

rear seats of my 911? <- ->

This is a difficult problem to which there seems to be no perfect solution. When our kid was born

(1987), we had a car seat made by Kolcraft; it seemed to fit okay into the skinney rear seat but it

hung over the front of the seat a little. In retrospect, this was probably unsafe. Thank heaven that I

never had this tested.

Several people have found that Porsche makes a seat to fit into the rear of a 911 but doesn't ship it

to the United States. This seat requires a 3-point seat belt (a lap belt PLUS a shoulder harness). I

can't state strongly enough that you don't what to compromise where safety is concerned. I don't

know why Porsche doesn't send their seats to the US, but is this a chance you're willing to take with

your child?

Mark Salvetti describes the seat:

It consists of four pieces, each sold separately: a seat bottom, a backrest (that straps

to the seat bottom), a shield or table that the seatbelt passes through and secures the

child across the thighs and midsection, and an insert that fits under the seat bottom

(928/944/968 only).

The parts you need depend on weight ranges: for 9 kg to 18 kg you need all the

pieces, for 15 kg to 25 kg you don't need the backrest, and for 15 kg to 36 kg you

only need the bottom. The part numbers are: 000 802021002CZ for the seat bottom

and 000 802041002CZ for the table. We didn't need the backrest, so I don't know

the part number.

[...]

I doubt the European seats are approved by DOT, NHTSA, etc. Also, I am not

advocating using the above child seat against the instructions with only a lap belt. Do

so at your own risk.

Mark Salvetti. mark_salvetti@ABBSMTP.abb.com "Re: 911 Baby Seats (long)", 26 Jun 96.

Message-Id: <9605268358.AA835827015@ABBSMTP.ABB.COM>

Mark also said that you can buy the seat for 175 British Pounds from AFN, a dealership in

Cheswick, England. You can reach them at 011-44-1-81-742-7700.

Todd Cohen found another partial fit:

For the few times that I drove my daughter around in the 911, I was able to use the

existing car seat that I had. I had a Century 2600 seat, to install it in the 911 I removed

the rear cross bar, by removing one bolt. This allowed the seat to fit in the cupped rear

seats.

Todd Cohen. TODD.COHEN@rdd.com "911's and Baby Seats", 25 Jun 96. Message-Id:

<0013600001837344000002*@MHS>

Q3.6. Any other places I can look for 911

info? <-

I know nothing about alignment but you can check out Mike Piera's web page for his take on this.

There's also a bunch of useful information at the Poor Man's Porsche site.

References.

Porsche 911 Performance Handbook, Bruce Anderson, Motorbooks International, 1987

Guide to Purchase & DIY Restoration of the Porsche 911, Porter and Morgan, Haynes

Publishing, 1988

The 911 and 912 Porsche, a Restorer's Guide to Authenticity, Dr. Brett Johnson, Beeman

Jorgensen, Inc., 1988, 1991

Original Porsche 911, Peter Morgan (et.al.), Bay View Books, 1995

Illustrated Porsche Buyer's Guide, 2nd Edition, Dean Batchelor, Motorbooks International,

1983, 1986

Road & Track Porsche, CBS Magazines, 1988

Road & Track Porsche, CBS Magazines, 1990

New For '95, Road & Track, October 1994, Hachettte Filpacchi Magazines, Inc, 1990

Miscellaneous Articles, lance_keigwin@engtwomac.Synoptics.COM, mpardo@itsa.ucsf.EDU,

911 #1, Excellence, November 1994, Don Hollway

The Used 911 Story, Peter Zimmerman, PMZ Publications, 1993

This FAQ written and maintained by

Wade Guthrie, guthrie@deltanet.com