924/944/968 Frequently Asked Questions

Version 1.4

Welcome to the PorscheFans 924/944/968 list's FAQ, a compendium of "Frequently Asked Questions."

1.0 Introduction

2.0 Model Outline

3.0 Production and Import Figures

4.0 Model Information

5.0 First-Time Buyer Questions

6.0 Interior/Body

7.0 Cooling System and Related

8.0 Engine

9.0 Clutch & Transmissions

10.0 Suspension and Related

11.0 Miscellaneous Engine Compartment

12.0 Electrical

13.0 Performance Modifications

14.0 924/944/968 Resources

15.0 Copyright Notice

_______________________________________________________________________________

1.0 Introduction

The goal of this FAQ is to provide answers to frequently asked questions about four-cylinder,

water-cooled Porsches. These questions have been posted to the PorscheFans mailing list, which

provides an on-line community for Porsche owners and fans throughout the world. If you would like

to subscribe to PorscheFans, click here to learn how.

This FAQ is a work in progress. If you have any suggestions, additions or clarification, please

e-mail me at kgross@connact.com. The information is from many sources, mainly "the list

consensus". If you don't agree with something or feel something is blatantly wrong, please send me a

note with a correction. Special thanks to Dennis Mitsch, Michael Kehr, Bob Joyce, and all the rest

who helped this FAQ get off the ground!

1.1 A Little History

This FAQ originated with the Porschephiles mailing list. Since then, Porschephiles has disappeared.

A new mailing list has taken its place, however. PorscheFans can be found at

http://www.porschefans.com, and that page gives instructions on joining the PorscheFans discussion

group. There is a 924/944/968 specific group.

1.2 Who Wrote the FAQ

A number of folks have helped create and maintain this document. The current FAQ maintainer is

Kevin Gross, who can be reached at kgross@connact.com. Dennis Mitsch, Jim Pasha, Michael

Bremer, Clint Cummings, H. Shrikumar, Michael Kehr, Bob Joyce, and many others have

contributed to the care and feeding of the FAQ and to the authorship of the information contained

within it.

2.0 Model Outline

The four-cylinder, water-cooled Porsche has been through twenty odd years of development. The

following table summarizes the models.

2.1 The 924

Year                                            1976                                     1977                                     1977

Engine Code                              XK                                    XH, XK                                XG, XE

Displacement  (cc.)                  1,984                                     1,984                                    1,984

HP @ RPM  (DIN)             125 @ 5800                            100 @ 5500                         115 @ 5500

Stroke/bore  (mm).              84.4 x 86.5                                84.4 x 86.5                            84.4 x 86.5

Compression  ratio                9.3 : 1                                         8.0 : 1                                  8.5 : 1

Management system               CIS                                             CIS                                     CIS

Transmission Code                088/6                                           088/6                                  088A

Weight (lb.)                             2,344                                           2,344                                  2,344

Chassis numbers       9246100001 – 924610645       9247200001 – 9247235789                  ???

________________________________________________________________________________

Year                                            1978                                     1979                                     1980

Engine Code                           XG,XE                                    XH, XK                                VC

Displacement  (cc.)                  1,984                                     1,984                                    1,984

HP @ RPM  (DIN)             115 @ 5800                            100 @ 5500                         115 @ 5500

Stroke/bore  (mm).              84.4 x 86.5                                84.4 x 86.5                          84.4 x 86.5

Compression  ratio                8.5 : 1                                         8.0 : 1                                 9.0 : 1

Management system              CIS                                           CIS                                     CIS

Transmission Code               088A                                        016/Y                                  016/9

Weight (lb.)                           2,344                                         2,344                                   2,344

Chassis numbers       9248200001 –                           9249200001 –                         92A0430001 –

________________________________________________________________________________

Year                                       1980 Turbo                                  1981                               1981 Turbo

Engine Code                           M31/02                                      VC                                     M31/04

Displacement  (cc.)                  1,984                                     1,984                                      1,984

HP @ RPM  (DIN)             150 @ 5500                            115 @ 5500                         156 @ 5500

Stroke/bore  (mm).              84.4 x 86.5                                84.4 x 86.5                            84.4 x 86.5

Compression  ratio                7.5 : 1                                       9.0 : 1                                  8.5 : 1

Management system               CIS                                          CIS                                     CIS

Transmission Code                G31/02                                     016/9                                  016/G

Weight (lb.)                             2,719                                       2,344                                   2,719

Chassis numbers             93A0150001 –                        92BM450001 –                    93BM150001 –

________________________________________________________________________________

Year                                         1982                                    1982 Turbo

Engine Code                            VC                                       M31/04

Displacement  (cc.)               1,984                                      1,984

HP @ RPM  (DIN)           115 @ 5500                            156 @ 5500

Stroke/bore  (mm).              84.4 x 86.5                             88.5 x 86.5

Compression  ratio               9.0 : 1                                      8.0 : 1

Management system            CIS                                          CIS

Transmission Code             016/9                                       016/G

Weight (lb.)                         2,344                                        2,719

Chassis numbers        92CN450001 –                          93CN150001 –

________________________________________________________________________________

2.2 The 924 S

Year                                           1986                                          1987                               1988

Engine Code                           M44/07                                   M44/07                           M44/09

Displacement  (cc.)                  2,479                                       2,479                                 2,479

HP @ RPM  (DIN)             158 @ 5900                            158@ 5900                         158 @ 5900

Stroke/bore  (mm).              78.9 x 100.0                            79.8 x 100.0                        79.8 x 100.0

Compression  ratio                10.2 : 1                                     10.2 : 1                              10.2 : 1

Management system               DME                                       DME                                 DME

Transmission Code                  016J                                         016J                                   016J

Weight (lb.)                               2,627                                        2,627                                  2,627

Chassis numbers              92GN400001 –                          92HN450001–                   92JN450001 –

_______________________________________________________________________________

2.3 The 944

Year                                           1983                                          1984                               1985 –

Engine Code                           M44/02                                   M44/02                           M44/02

Displacement  (cc.)                  2,479                                       2,479                                 2,479

HP @ RPM  (DIN)             150 @ 5500                            150@ 5500                       150 @ 5500

Stroke/bore  (mm).              78.9 x 100.0                            79.8 x 100.0                      79.8 x 100.0

Compression  ratio                9.5 : 1                                        9.5 : 1                                 9.5 : 1

Management system               DME                                      DME                                 DME

Transmission Code                  016K                                     016K                                   016K

Weight (lb.)                               2,675                                      2,675                                  2,675

Chassis numbers             94DN450001–                          94EN450001–                   94FN470001 –

_______________________________________________________________________________

Year                                           1985 +                                      1986                              1986 Turbo

Engine Code                           M44/07                                   M44/07                              M44/51

Displacement  (cc.)                  2,479                                       2,479                                 2,479

HP @ RPM  (DIN)             150 @ 5500                            150@ 5500                         217 @ 5800

Stroke/bore  (mm).              78.9 x 100.0                            79.8 x 100.0                        79.8 x 100.0

Compression  ratio                9.5 : 1                                      9.5 : 1                                  8.0 : 1

Management system             DME                                       DME                                 DME

Transmission Code                016K                                      016K                                 016R

Weight (lb.)                             2,637                                        2,637                                2,758

Chassis numbers              94FN450001–                       94GN450001–                   95GN150001–

_______________________________________________________________________________

Year                                           1987                                       1987 S                          1987 Turbo

Engine Code                           M44/07                                   M44/40                            M44/51

Displacement  (cc.)                  2,479                                       2,479                                 2,479

HP @ RPM  (DIN)             158 @ 5900                            188@ 6000                         217 @ 5800

Stroke/bore  (mm).              78.9 x 100.0                            79.8 x 100.0                        79.8 x 100.0

Compression  ratio                10.2 : 1                                  10.9 : 1                                 8.0 : 1

Management system               DME                                    DME                                  DME

Transmission Code                  016K                                    083D                                  016R

Weight (lb.)                               2,637                                     2,637                                  2,758

Chassis numbers              94HN470001–                          94HN450001–                   95HN150001–

_______________________________________________________________________________

Year                                           1988                                       1988 S                          1988 Turbo

Engine Code                           M44/09                                   M44/40                           M44/51

Displacement  (cc.)                  2,479                                       2,479                                 2,479

HP @ RPM  (DIN)             158 @ 5900                            188@ 6000                         217 @ 5800

Stroke/bore  (mm).              78.9 x 100.0                            79.8 x 100.0                        79.8 x 100.0

Compression  ratio                10.2 : 1                                     10.9 : 1                              8.0 : 1

Management system               DME                                      DME                                DME

Transmission Code                  016J                                      083D                                  016R

Weight (lb.)                               2,637                                      2,637                                 2,758

Chassis numbers              94JN470001–                          94JN450001–                  95JN150001–

_______________________________________________________________________________

Year                                      1988  Turbo S                          1989                            1989 Turbo

Engine Code                           M44/52                             M44/11,12                          M44/52

Displacement  (cc.)                  2,479                                   2,688                                 2,479

HP @ RPM  (DIN)             250 @ 5800                         162@ 5800                         247 @ 6000

Stroke/bore  (mm).              78.9 x 100.0                         78.9 x 104.0                        79.8 x 100.0

Compression  ratio                8.0 : 1                                   10.9 : 1                              8.0 : 1

Management system            DME                                     DME                                 DME

Transmission Code              016R                                      016J                                   016R

Weight (lb.)                            2,758                                     2,637                                  2,758

Chassis numbers              97JN50001–                      94KN450001–                  95KN150001–

_______________________________________________________________________________

Year                                           1989 S                                   1989 S2                         1990  (S2)

Engine Code                           M44/41                                   M44/41                           S2M44/51

Displacement  (cc.)                  2,688                                       3,000                                 3,000

HP @ RPM  (DIN)             188 @ 6000                            208@ 5800                         208 @ 5800

Stroke/bore  (mm).              78.9 x 104.0                            87.8 x 104.0                        87.8 x 104.0

Compression  ratio                10.9 : 1                                     10.9 : 1                              10.9 : 1

Management system               DME                                       DME                                 DME

Transmission Code                  083F                                         083F                                083F

Weight (lb.)                               2,637                                        2,637                                  2,857*

Chassis numbers              94KN450001–                         94KN480001–                  94LN450001–

______________________________________________________________________________

Year                                           1991 S2

Engine Code                           S2M44/41

Displacement  (cc.)                  3,000

HP @ RPM  (DIN)             208 @ 5800

Stroke/bore  (mm).              87.8 x 104.0

Compression  ratio                10.9 : 1

Management system               DME

Transmission Code                  083F

Weight (lb.)                               2,857

Chassis numbers              94MN450001–

* Cabriolet weight: 2968 lb.

2.4 The 968

______________________________________________________________________________

Year                                           1992 and 1993

Engine Code                              M44.43/44

Displacement  (cc.)                       3,000

HP @ RPM  (DIN)                   236 @ 6200

Stroke/bore  (mm).                   87.8 x 104.0

Compression  ratio                    11.0 : 1

Management system                 DME

Transmission Code                   G440

Weight (lb.)                                 3,086**

Chassis numbers              1992:  96N820061-

1993:  96PS820061-

* Coupe Tiptronic: 3,152 lb.

* Cabriolet weight: 3,240 lb.

* Cabriolet Tiptronic : 3,306 lb.

3.0 Production and Import Figures

The following figures are from two sources, courtesy of Michael Bremer:

"Das grosse Buch der Porsche-Typen," by L.Boschen and J. Barth

"Deutsche Automobile seit 1945," by W. Oswald

My thanks to Michael for his help. Bear in mind that production figures have historically been

notoriously inaccurate. In particular, the factory has frequently created post- or extra-production

cars for special customers.

Because so many list members are from the US, and because the US and Japan production figures

are sometimes available, we have included where possible the number of units brought into these

countries.

3.1 The 924

Model Year         Production        Rest of World            USA                Japan

1976                          5145                         5145

1977                        25596 *                    17675                    7496                  425

1978                        21562                         9474                   11638                 450

1979                        20619                       10475                     9636                 508

1980                        12794 †                      9094                     3700

1981                        11824 ‡                      9669                     2155

1982                        10091                         7814                     2277

1983                          5785                         5785

1984                          4659                         4659

1985                          3214                         3214

total                      121289                       83004                    36902             1383

* includes 3000 special edition "Martini" cars

† includes 1030 special edition "Le Mans" cars

‡ includes 1015 special edition "50 Jahre Porsche/Weissach" cars

3.2 The 924 Turbo

Model Year             Production                 Rest of World                 US                     Japan

1979                              2932                               1982                          950

1980                              5243                               1803                        3440

1981                              3312                               1783                          586                      943

1982                              1819                                 876                          943

1983                                310                                 310 †

total                            13616                              5568                         6795                      943

† cars brought only into Italy

3.2 The 924 Carrera GT

Model Year             Production                        Germany               Rest of World                 Notes

1980 GT                       406                                      200                               206               includes prototypes

3.3 The 924S

Model Year             Production                  Rest of World                       US                            Notes

1986                              3536                                  3536

1987                              8940                                  1993                              6947

1988                              4193                                  2003                              2190             prod.ended Sept. '88

total                            16669                                  7532                              9137

*There was also a sport package for the 924S, brought into the US, for which we have no

production data.

3.4 924 Special Production

Model Year                       Type                                    Production                        Notes

1978                          924 Rallye Turbo                                  4

1979                          924 Rallye Turbo                                  1

1979                          924 SCCA                                             16                         for US market

1979                          924 Group 4                                           1                    built up from street car

1980                          924 Le Mans GTP                                4

1981                          924 Carrera GTS                                  59                5 were Club Sport with cage, etc.

1981                          924 Carrera GTR                                  17

total                                                                                        101

3.5 The 944

Model Year             Production                        Rest of World                             US                      Notes

1982                             3921                                         3921

1983                           14633                                         9127                                    5506

1984                           26539                                         9921                                  16618

1985                           23720                                       17553                                    6167

1986                           17010                                         6109                                  10901

1987                           10689                                         2343                                    8346

1988                             5965                                         2226                                    3731                  8 to Aus.

1989                           10593                                         4941                                    5652

total                         113070                                       5614                                    56921

3.6 The 944 Turbo

Model Year             Production                  Rest of World                      US                             Notes

1985                              178                                    178

1986                          10273                                  2760                               7513

1987                            4955                                  1546 + 188 SP               3210 + 11 SP

1988                            4097 *                               1875 + 94 SP                 1874 + 98 SP     +126SP Canada                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                           +30 SP Aus.

1989                            4103                                  1333                               1385                        1385 Can

1990                            1251                                  1107                                 144

1991                              875 †                                875

total                         25107                                  9331                              14235                 30 Aus, 1511 Can

* includes 1000 Turbo S

† includes 625 Turbo Cabrio

"SP" designates a sport package option.

3.7 The 944S

Model Year             Production                        Rest of World                     US                     Notes

1987                              5862                                       2635                             3127                    100 SP

1988                              7074                                       1305                             5562         20 Aus, 188 SP Can

total                            12936                                       4040                             8688         20 Aus, 188 Can

3.8 The 944S2

Model Year             Production                        Rest of World                       US                      Notes

1989                                 ?                                              ?                                  970

1990                              3321                                        2872                               449

1991                              3118                                        2608                               510

total                                                                                                                   1929

3.9 The 944S2 Cabriolet

Model Year             Production                        Rest of World                    US                    Notes

1989                                 ?                                              ?                                16

1990                              3938                                       2114                          1824

1991                              1702                                       1140                            562

total                                                                                                               2402

3.10 944 Special Production

Model Year                   Type                                 Production                                              Notes

1981                   944 GTP/R Le Mans                            1

1986-1989             944 Turbo Cup                              150or more

3.11 The 968

Model Year

1992

1993

1994

1995

total

* We have no production data for the 968; sorry.

4.0 Model Information

924

The original 2.0 liter version was replaced in 86 with the 2.5 litre

version, using the engine and many features from the 944-series

cars.

924 Turbo

924 Carrera GT

924 Carrera GTS

A limited edition produced for racing.

924S

Has the 944 drive train in 924 body, lighter, more aerodynamic and faster than a regular 944. The

88 models had a "sport" option available - these cars make excellent autocrossers and are worth

more.

1981-1985.5 944

Introduced in the US as a 1983 model. These early cars are lighter than the later cars. The interior is

a transplant from the 924. These cars were largely based on the 924 Turbo in that the maintained

basically the same body (except for the larger wheel arches), the ventilated brake discs, and

suspension. The 5-speed gearbox was an Audi transplant, while the automatic was from VW.

The totally new engine was a 2.5L inline 4 developed at Porsche. This engine has been called 1/2 of

a 928 engine, in that they do share the same cylinder head, valves, and bore & stroke (the 944 4

valve, 959, and 928S4 all have the same valves, valve guides, valve angles, & combustion

chamber). The new engine utilized contra rotating balance shafts to cancel out vibration in the

relatively large four-cylinder engine. Optional sport package available that added Koni/Boge sport

shocks, front/rear sway bars. The forthcoming turbocharged version was originally intended to

replace the aging 911.

1985.5-88 944

Forged aluminum front lower control arms, redesigned interior. The steering wheel was also moved

slightly to give more leg clearance.

Radio antenna removed & flush bonded with the front windshield. Included a new height-adjustable

steering wheel. Improvements in air vent flow, oil sump capacity, new front & rear cast aluminum

wishbones & trailing arms, larger fuel tank, battery moved to the rear, optional heated & power

seats, revised starter, revisions in the mounting of the transaxle to reduce noise & vibration. In 87,

ABS became standard & a new sport suspension package based on the Turbo Cup series became

available.

1989 944

Larger 2.7 liter engine for the last year for the standard 944. This is the only year of production of a

4 valve 2.7L engine.

1986-88 944 Turbo

87+ had dual air bags, ABS optional.

Utilized KKK's K26 turbocharger, an external oil cooler, and an air-to-air intercooler. Featured

Bosch Motronic engine management, an all new front end and rear under-valence panel (new body

pieces allowed the car to reduce the drag coefficient to 0.33), updated brakes, forged pistons, and

larger spring-centered clutch. The head was also beefed up in that it received stronger valves &

improved ports.

1988-89 944 Turbo S

The Turbo S engine is based on the normal Turbo engine. It's equipped with a modified turbo with

redesigned vanes. The DME computer has different fuel/ignition/boost mapping to give higher boost

over the entire RPM range compared to the normal Turbo. The exhaust valves were also increased

in diameter by 1/100th mm near the valve guide for better running at full load.

Water hose, pipe, mounts and turbo waterpump were all changed due to the reinforcements of the

front end. The clutch had changes in springs and the friction liner is cemented and riveted to handle

the extra power. Front and rear shocks are stiffer, the brakes are from the 928 S-4. Larger anti-roll

bars and torsion bars. The transmission has a limited slip and an oil cooler. 1st and 2nd gears were

hardness blasted for increased strength. "S" coil springs are also harder and tempered to allow for

wheel clearance. It also had harder rubber suspension bushings all around. Dual airbags and ABS

were standard.

1986.5-89 944S

Sixteen-valve head gives more power. Dual airbags standard for all years. ABS optional.

1989.5-92 944S2

Larger (3.0 liter) sixteen-valve engine, more torque at low RPM.

1989-92 944S2 Cabriolet

Convertible version of S2.

1993-95 968

6 speed, revised body style, variable valve timing.

1993-94 968 Cabriolet

Convertible version of 968. 1989 and later all models come with dual airbags standard.

5.0 First-Time Buyer Questions

5.1 What should I look for, do, or ask about, when considering a prospective car?

Complete maintenance records. These cars will treat you very badly if you don't take care of them.

Correcting one or two problems that the previous owner skipped can easily surpass any cost

savings you may have received by buying a car that was not maintained regularly.

Find a nice car. If the car looks good and is well taken care of, the odds are the rest of the

mechanical bits were well taken care of as well. Some models are rarer then others, but generally

there are a great deal of water coolers out there. Take your time, and find a great one.

Pre-sale inspection. Unless you're a Porsche mechanic, you should invest the $75-100 to take your

prospective car to one and have them look at it. This will give you an excellent idea of what sort of

costs you will be incurring over the next year or so, or even if the car is worth buying at all.

5.1.5 What are the areas to look for?

There are several common failure points on the 924/944s. To begin with visually inspect the car for

obvious signs of accident damage. Accidents can lead to costly repairs on items that are not

immediately visible. Check to make sure that all body panels line up correctly and that there is a

consistent spacing between all panels. These cars also have many problems with leaks in the hatch

area, around the sunroof, and in the passenger footwell. Check around for leak stains and rusting of

metal parts. Drive the car, and pay attention to how the engine idles, the amount of engine vibration

present, and the amount of backlash present in the drivetrain in manual cars. (These problems will

be explained in detail in section 5.4)

5.2 How do I tell if the 944 I'm looking at is early or late 1985?

Early 944's have the 924 instrument cluster. It's more boxy/squarish then the newer 944 panel. The

suspension arms on the early 944's were made of steel with replaceable ball joints. Later 944's use

aluminum arms with non-removable ball joints. To identify the vehicle for sure, you can examine the

VIN number. Early 944's had a VIN series beginning with 94FN47, later cars began with 94FN45

(the VIN tag is located on the driver's side windshield pillar by looking down from outside the car).

5.3 What is a 951? Is this some Porsche I haven't heard of before?

No, it's simply the factory designation for the 944 Turbo.

5.4 What are common failure modes, and how are hard/expensive are they to fix?

5.4.1 Timing Belt

It's important to have the belts replaced and tensioned regularly. If the timing belt fails, your valves

will be bent and you're in for a very expensive repair. Tensioning the timing belt requires an

expensive special Porsche tension gauge, some owners use the more traditional "by hand" method

without any adverse affects but the general consensus is "better safe than sorry". 1987 and later

944's have a tensioning device built in that allows you to perform this operation without the special

gauge. Early belts are prone to failure, the updated part number has a .02 suffix.

The belts should be changed at least every 60K. If the car does not have service records indicating

that this has been done, allow for an extra $300-$500 to have the belts changed if over 50K. The

tool required for belt tensioning is the P9201 and it runs about $500. The tool should still be used

on the 87 and later cars with the automatic tensioner.

5.4.2 Motor Mounts

If you have excessive vibration at idle, and the vibration disappears around 1200 RPM, one or

more of your motor mounts may be bad. The mounts have been through several designs, when

updating your mounts, make sure you're getting the newest version (p/n 951 375 042 04) from the

944 Turbo. The bolt lengths have also changed with the updated part, so check for updated

hardware.

The right (exhaust side) mount takes the most punishment and usually goes first.

The repair is within the reach of the accomplished backyard mechanic, but requires some tools,

skills and patience. Motor mounts may "look" OK and still be bad. The normal advice is to look for

fluid leakage. However, usually the fluid has leaked and evaporated long ago. A better way to

check the mounts is to fashion a [ shaped piece of stiff wire so that the points of the wire are 60 mm

apart. Use this gauge to measure the distance between the top and bottom surfaces of the mounts. If

it is less then the 60 mm, replace them. If you have an older 944 and it's vibrating, replacing the

mounts will make you feel like you have a whole different car. Europroducts is the one of the

cheapest sources of mounts at $110/each. Their number is 800-962-0911.

5.4.3 Water Pump

If you notice any noise or leaking from your water pump it is probably bad and should be replaced

right away. If the pump fails entirely the fluid may leak on your belts and they will need to be

replaced as well, or if the pump seizes it will destroy the timing belt as well - which could lead to

very expensive valve damage.

The water pump replacement is particularly unpleasant because it requires pulling the timing and

balance belts to get to it. You may want to consider replacing the belts at the same time. Changing

the thermostat at this time is also a good idea as it's very difficult to get to otherwise. The water

pump has been updated several times. The current New factory part number is 951 106 021 10,

the factory exchange water pump is 951 106 921 X ($100.00 core charge). If you update to the

latest pump, you will also need the updated thermostat (p/n 944 234 160 00), otherwise you can

use the old style thermostat (p/n 944 106 129 05). The rebuilt pumps may not be the bargain they

appear to be, and some mechanics will refuse to even install a rebuilt pump because they've had so

many fail. (See section 7.3 for information on removing the thermostat snap ring.)

5.4.4 Oil cooler seal leak

The seals in the oil cooler will sometimes shrink due to age, changing oil types, etc. In 1987,

Porsche redesigned the seal causing many failures. The production was not corrected until 1991. All

models between 1987 and 1991 are extremely at risk for this failure, if they haven't been updated to

the latest part keep a very close eye on your coolant and oil. When the seal fails, it allows oil to

enter your cooling system, and coolant into your oil. If you check your oil and notice a chocolatey

brown froth on your dip stick, or if you notice brown residue in your coolant over-flow tank, you

should take it to the shop immediately and have the seals replaced, the radiator and coolant

passages will need to be cleaned with a degreaser and the oil changed. It's also highly

recommended that the lower-end bearings be replaced due to the accelerated wear caused by

water in the oil.

The very early models (until 84) also had problems with the oil cooler seals failing. Replacement is

easily accomplished, and the updated seal kit will cost around $30-$40.

5.4.5 Power Steering Fluid Reservoir Leaks

The clamps that hold the hoses onto the reservoir don't seem to do their job very well. Replacing or

tightening the clamps tends to solve this problem. You may also need to replace the small flexible

piece of hose (and clamps) that allows the power steering fluid return hose to go around the engine

block and underneath the oil filter. The easiest way to check for a leak here is to raise the headlights

so you can look down inside the nose of the car. The main reason for catching these problems early

is that if power steering fluid leaks down onto your suspension arms it may rot out your ball joints.

As of 1985.5 they can't be replaced individually, and the entire arm ($$$) must be replaced.

There is now an updated version of the fluid line that goes from the reservoir to the pump. the new

version does not go around the oil filter & attach to the water pump, but rather straight from the

reservoir to the pump. As mentioned before, fix this problem as soon as you notice it because it can

lead to costly ball joint & steering rack repairs.

5.4.6 Hood and hatch shocks worn out

Harmless, but inconvenient. They can be replaced easily, they cost between $12-20 depending on

where you buy.

5.4.7 Hatch electronic release non-functional

The nylon piece that holds the cable sometimes breaks. This component is fairly easy to replace.

The carpet can also interfere with the rotating shaft. If the hatch is not aligned properly the hatch

catches will bind, not allowing the motor and associated cable to do it's job.

The hatch retaining pins can also become out of alignment, causing the release not to function. The

pins are adjustable, but if they are lengthened too much they can allow the hatch to leak.

5.4.8 Power window motor mechanisms

If the channels become dirty or warped, the power window motors may become damaged and

eventually burn out. If the motor sounds like it is straining, or makes grinding/lugging noises it will

more than likely need to be replaced in the near future. Cleaning the channels and making sure the

windows are properly aligned will prevent damage.

5.4.9 Idle Stabilizer

Gets gunked up and causes rough idle. Some list members have disassembled the idle stabilizer and

successfully cleaned them up. On the 944 turbo and 944S the intake manifold must be removed to

access the stabilizer(this can be expensive labor wise). An updated part is available which is

supposed to minimize the problem. It's manufactured by Bosch and replacement cost is

approximately $175.00.

5.4.10 Fuel Injectors dirty

Porsche Cars North America (PCNA) recommends that you use a product containing the Chevron

Techron additive to keep injectors clean and fully functional. If you notice hard starting, rough idle,

or weak acceleration you may want to try running a bottle of this additive to your next fill up of gas.

5.4.11 Front wheel shimmy

A shimmy at around 70 mph on early 944's appears to be a very common problem. No one is sure

why it exists, but it may have something to do with the front suspension's VW rabbit origins. A

wheel-on-the-car balance job frequently helps minimize the problem.

5.4.12 Cruise Control Problems

Symptoms such as: doesn't set speed, speed fluctuates, speed increases, etc. are generally caused

by a bad cruise controller. The control box is above the hood release catch inside the car. It looks

like a long, thin, rectangular metal box. Apparently one or more components can go bad inside,

which leads to all kinds of intermittent problems. This is not the only thing that can go wrong with the

cruise control system, but is very common. If possible, have your mechanic or a friend with the

same car swap boxes and see if it fixes your problem.

(Note: if anyone has information on repairing CC boxes, please let me know so I can add it to the

FAQ.)

5.4.13 Worn/leaky heater valves caused damage to clutch

The heater valve has been moved to a different location (above the oil filter) in later models. The

retrofit can be done by a novice mechanic. New hoses must be ordered. The changeover occurred

in approximately 1988/89.

5.4.14 Coolant tank expanding

Age and high temperature combine to make the coolant overflow tank swell and eventually fail.

Replacing it before it fails entirely would be a very good idea. They run around $120 new.

5.4.15 Turbo Coolant Pump

This pump is supposed to run for 30 seconds after the car is shut off, circulating water through the

turbocharger. You can hear it running if it is operating properly. The pump is assembled in two

sections, with age and heat the motor shaft binds and stops working. The hoses at the bottom of the

pump create stress and this can cause a misalignment of the motor shaft. Readjusting the pump

housing in the pump clamp may unbind the pump. A replacement unit runs about $175.00. (p/n 951

606 130 01)

5.4.16 Cracks in old style manifolds (non-accordion type)

Under warranty PCNA replaced the non-bellowed type headers when they cracked, with the

improved accordion style. The factory changeover occurred sometime in 1987. If you have an 86

with cracked bellowed-type headers, a lot of complaining may get them replaced under the "hidden"

warranty even if it's beyond the normal warranty mileage. Otherwise, replacement would cost

roughly $1200.00.

5.4.17 Center console cassette holder hinge broken

A very bad design and a very common failure. The official Porsche component is used to be very

expensive. Recently PCNA made available the hinge-only part (944 552 553 01 01C) which is

much cheaper (approximately $13). Steel after market replacements are also available.

5.4.18 Cracked or Broken Windshields

The 944 windshield is particularly expensive, the list price is over $2000! If you don't live in a major

city with many glass places, you may want to mail order the glass and have one of the local glass

people install it:

Prices as of 2/95:

1977-1984 $256.00

1985-1991 $445.00 with antenna

1990-1993 $365.00 convertible and with antenna

Discounts @ Glass Suppliers, 1-800-421-1414

5.4.19 Cracked Dashboards

A very common cosmetic annoyance. Gary Cook (gary.cook@Sun.COM) researched various

places that rebuild dashes. The price ranges were from $300-450.

Dash Specialists

1910 Redbud Lane

Medford, OR 97504

(503) 776-0040

The Newdash Group

4747 E. Elliot St. Suite 29

Phoenix, AZ 85044

(800) 283-2744

(602) 893-3030

Just Dashes, Inc

5941 Lemona Ave.

Van Nuys, CA 91411

(800) 247-DASH

(818) 780-8005

(818) 780-9014 (FAX)

5.4.20 Leaks in the passenger cabin

These cars are prone to leaks into the passenger cabin that usually originate from one of three areas:

the sunroof, the hatch, and the passenger side footwell.

Leaks from the sunroof are usually caused by stopped up drain hoses. These hoses allow the water

that accumulates in the drain canal around the sunroof to run out. Check to make sure that there is

no debris in the tubes that will stop them up.

The hatch can also leak. Leaks here are usually caused by a worn out hatch seal, stopped up spoiler

drains, or a combination of the two. A new hatch seal costs around $60. The spoiler drains are the

small rectangular holes on each corner of the spoiler. These can become clogged up, allowing water

to back up & spill over the hatch seal. Replacement of the hatch seal and cleaning the drains will

usually solve these leaks.

The final problem area of the 924/944 with leaking is the passenger footwell. The problem occurs

when the battery leaks acid onto the battery tray (located directly above the passenger footwell in

the engine compartment) and rusts it out. Eventually, the tray rusts completely through & allows

water to enter the passenger cabin. The best way to repair this problem is to have a new piece of

metal welded into place in the battery tray; however, this is expensive (around $500). Some have

fiberglassed the tray with some success, but usually the leak will return eventually. If this has not

already occurred to you, use a battery mat to absorb the battery acid & prevent the rusting. This

does not apply to the newer models with the battery located in the rear.

5.4.21 Clutch

The 944 originally had a problem with the rubber centered clutch fracturing, allowing the center to

move about freely & inducing a lot of freeplay to the drivetrain. If you notice a substantial amount of

backlash when engaging or releasing the clutch, chances are that the clutch needs to be replaced.

This repair will run around $1200 at a shop, or you can purchase the required parts for around

$550. There are now updated versions of the clutch disc for these rubber-centered versions

consisting of a spring center.

5.5 What are the available option codes?

Option codes are located on a sticker in the spare wheel compartment. The following aren't

necessarily all 924/944/968 option codes, but most of 'em should be in here. Thanks to Mike Tietel

for his huge list!

C02       Catalytic Converter

C03

C77

R01       Touring Package (Not Available w/ Airbags)

R74       Touring Package

009        Sporto-matic transmission

018       Leather STR Wheel/Raised Hub 380MM(Not Available w/ Airbags)

020       Speedometer with 2 scales KPH/MPH

024       Version for Greece

026       Activated charcoal canister

027       Version for California

030       Club Sport Package

031       Sport shock absorbers

034       Version for Italy

036       Bumpers with impact absorbers

058       Bumpers with impact absorbers

061       Version for Great Britain

062       Mud flap (version for Sweden)

070       Tonneau cover - Cabriolet

103       Adjustment of shock absorber strut

113       Version for Canada

119       Version for Spain

124       Yellow light (version for France)

126       Stickers in French

130       Labeling in English

139       Heated Seat Left

152       Engine noise reduction

153       Engine parts belonging to a stipulated assembly for type 951

154       Control unit for improved emissions

157       Oxygen sensor and catalyst

158       Radio "Reno"

160       Radio "Charleston"

164       Tires 215/60 VR15

176       Oil cooler with fan

185       Automatic 2 point rear seat belts

186       Manual 2 point rear seat belts

187       Asymmetric head lights

190       Increased side door strength

193       Version for Japan

195       Prepared for cellular telephone

197       Higher amperage battery

215       Version for Saudi Arabia

218       License brackets front and rear

219       Differential

220       Limited Slip Differential

221       Porsche-locking differential

225       Version for Belgium

240       Version for countries with inferior fuel

241       Shorter shifting travel

243       Shorter gear shift lever

249       Automatic transmission

255       Fuel consumption indicator

258       Heating for outside mirror

261       Passenger side mirror - electric - plain

262       Outside mirror for passenger side, plain, manual

277       Version for Switzerland

286       High intensity windscreen washer

288       Headlight Washers

298       Prepared for unleaded fuel, manual transmission

302       Type designated on rear end

308       Pneumatic spring for engine hood

323       Sticker, without ESE-Regulations

325       Version for South Africa

330

331       AM/FM Cassette w/2 door speakers

335       Automatic 3 point rear seat belts

340       Heated Seat Right

341       Central Locking System

346       Standard color rims (silver)

347       Platinum anodized wheels

348       Forged wheels - Grand Prix White

351       Porsche-car radio, CR stereo, type DE

360       Mud Guards

375       Clutch lining without asbestos

377       Combination seat, left, adjustable

378       Combination seat, right, adjustable

379       Series seat, left electrical vertical adjustment

380       Series seat, right electrical vertical adjustment

381       Series seat, left

382       Series seat, right

383       Sport Seat Left w/Elec. Height. Adj.

387       Sport Seat Right w/Elec. Height. Adj.

389       Porsche-car radio, CR stereo, type US

391       Stone guard foil, added separately

393       Forged Alloy Wheels-8/9x16 (944/944S) (944 Turbo)

394       Pressure Cast Magnesium Rims (944/944S) (944 Turbo)

395       16" Forged Alloy Wheels (944/944S) (944 Turbo)

396       Disk wheel, telephone styling 8Jx15 rear

398       Outside Electric Mirror, Left

399       A/C without front condenser

400       Pressure cast wheels

401       Light metal wheels

402       50 year anniversary car 1982

403       Pressure cast 17" wheels

404       Stabilizer Bars Front & Rear

405       Level control system

406       50 year anniversary car 1982

406       Front wheel housing protection 1983-1986

407       18-inch polished wheels

409       Sport seats left and right leather

410       Sport seats left and right leatherette/cloth

411       License bracket, front

412       External oil cooler

414       External Transmission Oil Cooler (Turbo)

415       Wider rear track

418       Body Side Molding

419       Rear luggage compartment instead of rear seats

422       Porsche-car radio, CR stereo, type RW

423       Cassette container and coin box

424       Automatic heating control

425       Rear Window Wiper

426       Special model World Champion 1976 1978

429       Fog headlamp, white

429       Special model "Sebring"

431       Leather Steering Wheel 363MM (Not Available w/Airbags)

432       Sports steering wheel, leather 363mm (4 spokes)

437       Full Power Seat Left

438       Full Power Seat Right

439       Electric Cabriolet top

439       Special model "Weissach" 1980

440       Manual antenna, 4 speakers

441       Fader, antenna booster, 4 speakers

441       Radio speakers and antenna amplifier

442       Prepared for radio without antenna

443       Tinted front and side glass, heated windshield

444       Cabriolet

446       Parts for type "Targa" belonging to stipulated assembly

447       Emergency wheel - with collapsible tire

450       Light metal wheels

451       Prepared for radio for sport group

454       Automatic Speed Control

455       Wheel locks

458       6" Cast Alloy Wheels

461       Electric antenna, 4 speakers

462       Special model "Weissach" 1982

462       Sekuriflex windshield

463       Clear windshield

463       Lateral glasses tinted, (version for Australia)

464       Without compressor and tire pressure gauge

465       Fastening parts for transportation (version for overseas)

467       Drivers side mirror, convex

468       Graduated tint windshield, green side glass

469       Black headliner

470       Without spoilers, in conjunction with turbo look

471       Sport group 1

471       Integrated rear spoiler

472        Rear Apron

473       With spoilers

474       Sport Shock Absorbers

475       Brake pads without asbestos

475       License plate fastening (version for Austria, Finland, Australia)

476       Brake pad with abrasive pad

479       Version for Australia

481       5 speed manual transmission

482       Engine compartment light

483       Right hand drive

484       Symbols for controls

485       Forged wheels – gold metallic

487       Connection for fog headlamp with parking light

488       Stickers in German

489       Symbols and insignia in German

490       Sound Package

491       Turbo look

492       H4 headlights for left hand traffic

494       Amplifier System

494       2 speakers on back shelf

496       Black trim – painted headlight rims

498       Delete Model Designation-Rear

499       Version for West Germany

503       Cabrio variant (Speedster)

505       Slant nose

513       Lumbar Support-Right Seat

525       Alarm with continuous sound

526       Door Panels Covered w/Cloth

528       Passenger side mirror convex

529       Outside mirror – passenger side, convex, manual

533       Alarm System

537       Left seat with positrol and lumbar

538       Right seat with positrol and lumbar

548       Fuel filler neck, unleaded fuel with flap

553       Version for USA

559       Air conditioner

560       Detachable roof

562       Airbag- Driver's Side

563       Airbag- Passenger's Side

565       Safety steering wheel - leather

566       Rectangular front fog lights

567       Windshield green graduated tint

568       Tinted windshield and side glass

570       High output air conditioner

572       Heating

573       Air Conditioning

576       Without rear fog light

586       Lumbar Support-Left Seat

592       Brake fluid warning system

593       Anti-Lock Braking System (ABS)

595       Rear spoiler painted to match body

596       Spoiler painted matte black

597       Heavy duty battery and starter

598       Insignia "16 ventiler"

602       Third brake light "High mount"

605       Vertical headlight adjustment

607       More numerous cables for dashboard

621       Differing parts for engine 924S

622       Differing parts for cars with 2 V-Engine

637       Performance Handling Package (944/944S) (944 Turbo)

642       Additive for cooling water

650       Electric Sunroof

651       Electric Windows

657       Power steering

659       Onboard computer

666       Without lacquer preservation and chrome preservation

673       Prepared for lead sealed odometer

675       Instrument cluster - technical lighting

684       1 piece rear seat

685       Divided rear seat

686       Radio "Ludwigsburg" SQM with arimat

691       CD-Player "CD-1" with Radio

692       Remote CD changer (6-disc)

701       Car-version Slant Nose

719       Special reconstruction

756       Special Model 924S USA 1988

757       Special model 944 1988

758       Special model 944 Turbo 1988

780       Remove safety certificate

900       Tourist delivery

912       Vehicle without identification plate

925       High altitude areas (version for US)

930       Seat cover rear LLL

931       Seat cover rear KKK

932       Seat cover rear SKK

933       Seat cover rear SLL

934       Seat cover rear SSK

935       Seat cover rear RLL

945       Seat cover front SKK

946       Partial Leather Seats Front

947       Seat cover front: cloth/leather/leatherette

Seat cover rear: cloth/leather/leatherette

948       Seat cover front SLL

974       Luggage boot cover

975       Velour carpet in luggage compartment

980       Seat cover – Raff – leather

981       Leather Interior (except seats)

983       Leather Seats-Front and Rear

985       Parts silver colored

986       Partial leather lining

989       Left and right sport seats - cloth

990       All Cloth Seats

OTE: Options 562 and 563 must be ordered together.

ption 637 must be ordered with option 030.

* Standard Equipment 944 Turbo.

6.0 Interior/Body

6.1 Where is the %$#@!! odometer trip reset switch?

The instructions are in your owner's manual. If you don't have an owner's manual, you may want to

consider purchasing one. It's chock full of handy information about your car. For the benefit of the

owner's manual impaired: "The trip odometer in the lower part of the speedometer can be turned

back to zero by pressing the reset-button, located in the left section of the center dashboard vent.

The ignition must be on." It looks like a half-sized vent air direction slider.

6.2 How do I get the sunroof off?

The owner's manual isn't quite complete in its description of how to remove the sunroof. The

proper sequence of events is:

Close the sunroof entirely.

Turn off car.

Turn the ignition key to the FIRST indent (IMPORTANT!).

Press the sunroof key, you should hear a noise from the sunroof.

Hold the button down until it stops. The roof is now unlatched.

Unhook the front manually, press up on the back and you should be able to remove the roof.

6.3 My sunroof/windshield/other leaks and my car is full of water, what do I do?

There are several ways for rain to turn your car into a bathtub. Some of the more popular ones are:

Sunroof

There are 4 drain holes located at each corner of the channel where the sunroof sits on the roof. If

they get clogged with debris it allows water to overflow into your car. Removing the sunroof and

dumping some water down each hole is the best way to determine which one is causing the

problem. Don't use compressed air to clean it out, it may cause the tube to detach entirely.

Drilling holes in the firewall to run wiring

Water runs down the firewall and into your nice little hole. You may be able to seal it up, but it will

probably start leaking again with the movement of the wires and vibration. Rerouting the wiring

elsewhere and plugging the hole will fix your leak for good.

Rear hatch seal fails

If your rear storage compartments are filling with water, it is possible that the hatch seal has failed at

the place where the hatch meets the roof.

The hatch retaining pins can also cause the hatch to leak if they are run out too far. The spoiler

drains may become clogged with debris and allow water to run in over the hatch seal, so be sure to

clean them out often.

Passenger footwell

The problem occurs when the battery leaks acid onto the battery tray (located directly above the

passenger footwell in the engine compartment) and rusts it out. Eventually, the tray rusts completely

through & allows water to enter the passenger cabin. The best way to repair this problem is to have

a new piece of metal welded into place in the battery tray; however, this is expensive (around $500

). Some have fiberglassed the tray with some success, but usually the leak will return eventually. If

this has not already occurred to you, use a battery mat to absorb the battery acid & prevent the

rusting. This does not apply to the newer models with the battery located in the rear.

6.4 What is the actual temperature indicated by the temperature gauge?

85.5 and previous:

Bottom of gauge: 40 degrees C

Start of rightmost block: 105 C

End of rightmost block: 120 C

85.5 to present:

Bottom of gauge (start of bottom mark): 40 C

End of bottom mark: 60 C

First slash mark: 80 C

Second slash mark: 100 C

Start of top block: 115 C

6.5 I'd like to replace my hood badge, how do I get that thing off?

The hood badge has a couple of pins on the back that fit into some plastic grommets. You can use a

gasket scraper or putty knife to CAREFULLY (very carefully, or your paint will be damaged) to

pry off the old badge and simply push on the new one.

6.6 My hand brake won't stay up/doesn't hold the car, what's broke?

If it doesn't stay up, something is probably frozen or broken inside the hand brake assembly. You

can take it apart (much easier with the driver seat out) and examine the components. Most likely the

ratchet release is frozen and can be freed with some penetrating oil, or the spring is gone/broken.

The lever itself can also be the cause of the problem. The release button on the end of the lever can

work its way loose, causing the lever not to engage the metal lock into place when pulled up. This

button simply screws onto a metal shaft inside the lever, so screw the button back on until tight and

the problem will usually be solved.

If your hand brake doesn't work well and the cable linkage looks good you may have worn out

your brake shoes. Yes, the parking brake has its own little brake shoes. Typically they last a long

time unless you drive around with the parking brake on. The list price is around $50/each and you

need four (p/n 928.352.097.10). You can find very good used ones, since they typically don't wear

very much.

6.7 My hatch is making noises, anything I can do?

Not a lot. As the ambient temperature drops, the evil things start to squeak even more. First check

and make sure the hinges aren't loose or losing the hinge pins. You can alleviate some of the noises

by adjusting the posts that hang down from the hatch. Hold the post and loosen the lock nut and

then screw the post in a bit. Do both sides equally and try closing the hatch, repeat until it doesn't

close anymore and then back off a turn.

If you're experiencing clunking, it's possible the hatch glass as separated from the frame. You can

take it to a windshield shop and have them reglue the glass, it's fairly expensive but cheaper than a

whole new piece of glass.

6.8 My alloys aren't very pretty anymore, anything I can do?

After several years of brake dust, harsh car wash detergents, etc., the clear coat on the alloy wheels

will discolor. The best method of returning them to their proper state is to have them professionally

refinished ($$$). However, you can get good results with the following procedure. Clean the wheel

with a Safe For Clear coat wheel cleaner. Use a paintbrush with half of the bristles cut off to get in

all the nooks and crannies (tape up the metal part, or you'll add more scratches then you remove).

Rinse thoroughly and wipe down with a terry towel to make sure you get rid of the any residual

dirt/brake dust. Take your favorite mild polishing compound (3M hand glaze, Meguiar's, etc.) and

gently rub the discoloration or streaking out.

It's very important to protect your alloys from brake dust. Brake dust is HIGHLY corrosive and will

pit and discolor your wheels. Using a quality car wax on your rims will make cleaning them much

much easier and protect them from dirt and brake dust. A spray wax or general purpose wax

(Pledge) is faster and more convenient but won't last as long - rewax often. Some discoloration

(from heat, for example) may not clear up with the polish method, your only choices are to repaint

or have them refinished professionally. The same is true if your clear coat has been scraped off or

damaged. Your other option is to have them polished, or chromed. Both have disadvantages.

Chrome is very delicate, especially since several intermediate layers of metal are required to bond

the chrome with the wheel alloy. Polishing and clear coating gives a similar finish, and is slightly more

rugged. However, when the clear-coat eventually fails the appearance of your rims will degrade

rapidly. Typical pricing is $100/wheel for refinishing(painting), $110/wheel for

polishing/clear-coating and $125/wheel for chroming.

6.9 I need to pull my car onto a flatbed, what do I attach the tow rope to?

There is nothing good on the front of these cars to tow by. Anything you attach that cable to

(suspension arms) could cause expensive damage. If you have a 944 Turbo style nose, you can

purchase a "Toe Eye" for a few dollars from your Porsche dealer. This is a very good item to keep

in your car at all times. The part number is: 951.722.101.00.

There is a point of attachment on the front end, but it is very delicate & will usually bend if the car is

tightened down too much. On the outside of the frame on each side of the front end is a flat bracket

with a hole cut out of it. It sticks down just in front of where the bottom skid pan bolts to the frame

(the part that sticks up from the rest).

7.0 Cooling System and Related

7.1 What anti-freeze should I use? The bottle says "safe for aluminum engines."

Although several list members use it, it is not recommended by Porsche. The bottles labeled "safe

for aluminum engines" still contain phosphates. The only approved anti-freeze are ones that

specifically state "Phosphate Free".

7.2 My car runs hot/temperature fluctuates, what are possible problems?

Check your temperature sender and gauge.

Make sure all the air is bled from the cooling system. There are a few tricks in getting most of the air

out when refilling. The sixteen-valve heads are prone to trap more air than the simpler 8 valvers.

Kevin Gross' trick for getting most of the air out when refilling involves leaving the bleeder valve

open while refilling, loading the system until the expansion tank is mostly full and then forcing the

coolant through until coolant comes out the bleeder valve (how do you force the coolant through?

Kevin performs mouth to mouth on the expansion tank, the rest of us can use a coolant system

pressure tester - a device which basically looks like a bicycle pump connected to a radiator cap).

You may have to repeat the fill/pressurize cycle several times before coolant comes out of your

bleeder valve. For all bleeding, make sure you crank the heater temperature control to the full open

position or you'll be there forever trying to get the air out.

Check hoses, pipes, and paths for blockage/leakage and verify water is getting in the radiator. If

your car is over heating, but the radiator remains cold it's possible either the radiator is blocked or

the thermostat is stuck shut. The thermostat recirculates the water until the engine is hot, and then

opens up to let the water into the radiator. If it's frozen shut you'll overheat but still see the normal

reading on the gauge.

Check fan (there are two) operation. There are two relays that affect fan operation. One controls

the one fan during normal operation and another that controls the other fan when the A/C is on.

Only one fan operates when the A/C is off, turning on the A/C activates the other fan. Neither fan is

necessary for highway cooling (in fact, they get in the way) so you may only notice over heating in

stop and go traffic. The fan switch in the radiator can fail with the fan off, or on. If the fans won't run

under normal conditions (sitting in traffic while your temperature climbs) the switch is probably stuck

off. If your fans continue to run long after you turn off the car, draining your battery, the switch is

probably stuck in the on position.

Many people have sent questions regarding problems with this thermofan switch, so I will explain

here. The thermofan switch is a plug that screws into the radiator just below the inlet for the upper

radiator hose. It has two wires attached to it. This switch monitors the temperature of the coolant in

the radiator & decides when to turn on the fans. At one point, the normal cooling fan will kick in,

and at the high temp point, it will turn on both fans. If your fans continue to run after shutting off the

engine & drain the battery or do not come on at all, chances are the thermofan switch is bad. It will

run you under $20, and you can get a "cooler" version that will turn the fans on much earlier (keeps

the car cooler during autox, stop & go traffic, etc.) To replace, drain the radiator, remove the switch

(it unscrews from the radiator -- takes a 1 1/8" wrench or it's equivalent) and replace.

Check coolant level. Ensure that air flow to and through the radiator is not blocked. Make sure your

water/antifreeze ratio is greater than 2:1.

7.3 I can't remove that %$#@!! thermostat snap ring! What tool do I use?

Removing the 944 thermostat snap ring is extremely difficult due to its location and configuration.

Ron Olsen has suggested a particular tool: Snap On PR5645A Snap Ring Pliers (45 degree with

.09" tips). It runs approximately $20.

Automotion also carries 90 degree snap ring pliers (around $45).

7.4 I'm losing coolant, what's going on?

The coolant system is closed. If you're losing coolant it's very likely something bad. Pressurizing the

cooling system may help you find the leak. Common leakages are the hose connections, water

pump, oil cooler, or even the radiator splitting apart (they're part aluminum and part plastic, the

seam sometimes fails). If you do find a leak, your best bet is to fix the problem. Avoid using

stop-leak products if at all possible since they may cause more problems than they fix such as

clogging passageways and causing blowouts.

Also, check the heater valve for leaking. As was mentioned above, avoid stop-leak as it can clog up

the radiator and the heater core. If the radiator is the cause, bite the bullet and replace it (cost

around $300-$400). I think that it is close to impossible to repair a cracked seam in one of these

(I've tried it...even epoxy didn't work), so your best bet is to go ahead and replace. This is an easy

job that can be accomplished with minimal tools and in an hours time.

8.0 Engine

8.1 Where should my oil pressure be at when cold? warm? idling?

When your car is cold, the oil is thicker. Normally this means when you first start your car the oil

pressure will be 5 bar at idle. After warming up the car (typically, it takes approximately twice as

long for the oil to reach operating range as your coolant does) it should drop to between 2 and 3

bar at idle.

You don't need to worry unless it drops to or below 1 bar. If the oil pressure sender fails, typically

the oil pressure will peg at 5 bar as soon as you turn the key to the on position.

8.2 I'm worried about my car starving for oil during hard cornering, is there a fix?

For highly modified vehicles pulling very high cornering G's, it is possible that the oil will slosh away

from the pickup causing the engine to starve for oil (read: big engine damage). The 89 944 Turbo

and S2 have an additional pan baffle to help avoid this problem.This part will fit other 944's. The

Oil Pan Baffle part number is 944.107.389.03 and runs approximately $65.97. This may not fix the

problem entirely, but it may help.

8.3 Do I need a special engine stand to hold a 944 motor?

Nope. A "normal" four-finger engine stand works fine. Be careful that the bolts don't go too far into

the block or they may damage the mounting points for the bell housing.

8.4 I'm replacing my timing belt, any helpful thoughts?

It's a good idea to get a feel for how the engine turns before changing the belts. Going one full

rotation at the crank pulley will give you a good idea of how the engine should "feel". When you've

completed the job you will be able to tell if the car is out of time because the resistance will be too

high. If you don't know how it should feel, you may end up damaging your valves with your breaker

bar.

For final tensioning, the engine should be at TDC minus 10 degrees, to find TDC remove the

distributor cap and cam sprocket housing while leaving the wires in place (this is a good time to

replace your cap and rotor). You now have a clear view of the timing belt on the cam sprocket

enroute to the tensioner and can begin looking for TDC (top dead center). Using a breaker bar half

inch drive with a 24mm socket and a mixed bag of adaptors/extensions, turn the engine over at the

crank pulley nut until you align the nick in the cam sprocket with the nick in the cam housing.

Because the cam turns at a 2/1 ratio with the crank, you must check the flywheel for the stamped

"OT". At the rear of the engine from the drivers side just before the firewall, you can peek down

and see at least one opening atop the clutch bell housing. Inside is the flywheel which you will see

moving if you turn the engine with your left hand. Atop and through that hole will be the letters "OT"

when TDC is reached. It will be one of the two times the cam marks align. There is also a mark at

the bottom of the flywheel under the car, that will point straight down when TDC is reached. From

TDC, turn the crank anticlockwise 1-1.5 cam teeth.

In order to replace the timing belt on the '87 or later cars, you need to remove the self-tensioner

assembly which is held in place by 3 bolts you can't see. The 3 you can see, you don't remove. The

bolts you need to remove roughly form a triangle around and behind the three bolts you can see

(which are for the tensioning sprocket, the one the assembly pivots on, and the one that freezes it in

place).

I also recommend getting a good manual (Chilton's or the factory manuals) to assist in this process.

Be sure to set the engine to TDC -10 degrees (as outlined above) before removing the belts. In

addition to the two reference points mentioned above, there are also alignment marks on both of the

balance shaft sprockets. Make sure that everything is aligned before removal. Once this is done,

R&R the belts (or go further & replace the tensioners/rollers if you are doing so at this time). When

replacing the belts, make sure that you keep the reference marks aligned! Being off on the camshaft

sprocket will result in valve damage; being off on the balance shaft sprockets will result in much

vibration from the engine. Tighten the belts, then use the special tension gauge to adjust (part $

P9201, cost around $500). I have never seen a consensus on the actual setting used...My local

Porsche repair shop said 4.0 on the timing belt, 2.7 on the balance, Jim Pasha wrote in excellence

4.0 on both, and Chilton's had something different (4.0-4.6 balance, 2.0 timing I think). I went with

Jim Pasha's advice & set both to 4.0. Afterwards, I could hear the balance belt whirring, so I reset

it to 3.2. This seems to have fixed the noise. Just my 2cents... Once you have an initial adjustment,

use your breaker bar & turn the engine over one full revolution. Check the tension again & adjust if

necessary (this step is necessary is that it will remove slack on the belts caused by the belt binding

on the sprockets or tensioners. Keep in mind that the belts need to be checked & adjusted at 2000

miles, earlier if necessary. Aftermarket belts have a tendency to stretch much earlier that the factory

versions, so they may need to be checked sooner. The timing belt should be set to 2.7 at the 2000

mile mark.

8.5 How do I tension the timing belt an 87 or later car using the built-in tensioner?

The self-tensioner on '87 and later 944, S, Turbo and S2 allows accurate tensioning of the timing

belt without tool P9201. The assembly achieves this by means of a spring whose preload is fixed to

create the proper tension while the engine is cold. Loosening the correct bolts frees the spring up to

do this task before retightening.

The entire job is done from above the engine. You gain access to the belts by removing various

things depending on which 944 variant you have. The 944, S, Turbo and S2 are all a little different.

In each case you are removing hoses or boxes which carry air. The 944 has a coolant hose which

may get in the way. The Turbo needs to have some of its plumbing removed.

Once you have a clear view of the top portion of the two piece plastic belt housing, remove the

10mm bolts holding it in place and finagle it out. You now have a view of the tensioner assembly

and belts. The belt should look fresh and not show cracking or shining.

The next phase would, by some, be considered optional. The factory workshop manual states that

the engine should be at TDC (top dead center) minus 10 degrees (about 1-1.5 cam teeth) before

the tensioning spring is released. This is because belt tension isn't always the same between the cam

and crank as the engine turns. It varies slightly. If being unable to find TDC discourages you, you

might still be better off releasing the spring than chancing a loose belt. A description locating TDC is

available above in the timing belt replacement tips.

The tensioner is the alloy arm roughly 6 inches long with three bolts sticking out. If you look behind

it, you'll see the spring. The assembly swings on the top bolt, has an elliptical opening on the locking

bottom right bolt and retains the tensioning sprocket with the bolt on the left.

Loosen the top 13mm bolt. Now, while watching the tensioning sprocket for movement, loosen the

locking 13mm nut. The sprocket should either not move or move slightly to the left and up against

the timing belt. If no movement occurs, take a 17mm closed end wrench slip it on the sprocket bolt

and put pressure down on the nut to make sure it is not seized/jammed. Lock the locking nut to the

designated torque (warning: it's not much). Install everything back at the proper torque and you are

all set.

8.6 What's all this about the infamous belt tensioning tool P9201?

Because of the catastrophic nature of timing belt failure (valves being destroyed), there is very little

room for error when tensioning the timing belts. The P9201 tool costs approximately $400, and it

appears there is no alternative tool (the search for such a beast has become the holy grail of water

cooler do-it-yourselfers everywhere).

The 1987 and later cars have a built in tensioner for the timing belt. However, it is still

recommended that the tool be used on the alternator and A/C belts. Some folks use the "by hand"

tensioning method, this requires a good "feel" for how tight the belts should be but it's your engine

and your decision.

As of 10/96, the cheapest price available on the P9201 was $425, available from Engine Builders

Supply Co. (they are on the web). Average price is around $500. The tool should also be used to

double check the self adjusters on 87 and later models (better safe than sorry...)

8.7 I'm experiencing a random power loss in my Turbo, what's up?

This appears to be a common problem, especially on the 89 Turbos. The normal boost is 1.2 bar. If

everything is operational, it will go to slightly above 1.8 bar. The most common problem is a bad

connection due to corrosion on the throttle position switch (located on the throttle body, forward of

the intake manifold). On one side is a cable that controls the throttle opening, and the other side is a

black plastic device that reads the throttle position. The connection to this device can become

corroded. Typically moving around the connector a bit will fix the problem temporarily.

Disassembling the connector, cleaning and putting on a coat of dielectric grease on it will fix it

semi-permanently.

9.0 Clutch & Transmission

9.1 When I release my clutch in neutral, I hear noises, is this bad?

Not usually. The transmission has several shafts that the gears move back and forth on. On the end

of one of these shafts is the 5th gear idler. This gear rattles back and forth because it has a larger

tolerance than the others. Porsche apparently stopped all warranty repairs for this noise because

there is no real repair - the larger tolerance is normal. The noise is particularly evident because it

vibrates the input shaft which is connected to the torque tube that runs up the middle of your car.

This creates a megaphone type effect that amplifies the noise.

If you're unsure if your particularly "noise" is normal or not, taking it to a mechanic who has looked

at a few 944's should clear the situation up for you. Some owners have expressed that using

Swepco transmission oil quiets down the rattle somewhat.

9.2 I'm replacing my clutch, any helpful hints?

Bleeding the clutch circuit can be quite an adventure. Using a positive pressure bleeding apparatus

like the Gunson E-Z Bleed kit ($35 and uses compressed air from a tire) helps a lot. Another useful

hint is to jack the back end of the car higher than the front while bleeding, this helps trapped air to

escape.

Replace all the parts, not just the obviously broken ones. You should purchase and install a new

friction disk, pressure plate, guide tube, throw-out bearing, and pilot bearing.

The flywheel does not normally need to be removed and resurfaced. If it has deep or uneven

grooving, such as is caused by a broken spring, you should consider resurfacing it. Check the spec

book for minimum thickness after machining, and replace the flywheel if it is too thin.

9.3 Is there a complete clutch replacement procedure for the 944/951?

Michael Kehr has written an astoundingly detailed clutch replacement procedure for the 944/951.

You can find a copy of his write-up at

ftp://www.mindspring.com/users/ccumming/Porsche/944/944.clu.

9.4 I have noticed a large amount of backlash in the drivetrain when engaging/ releasing the clutch. What causes this?

There are two types of friction disks used in 924 and 944 series cars. Normally-aspirated cars use

a friction disk which has a rubber center, basically a large puck that's fused to the disk and to a

splined tube. The disk is sandwiched between the pressure plate and the flywheel, from which it is

torqued by the running engine. Force travels through the rubber center to the splined tube, which is

located on the drive shaft, which in turn transmits engine torque to the transmission at the rear of the

car.

Instead of a rubber center, the turbocharged cars use a series of large and small coil springs within

the friction disk. This design is able to tolerate higher torque loads than the rubber center. The

disadvantage to the spring-centered design is that it transmits more mechanical shock to the

transmission.

With age or abuse, the rubber center in normally-aspirated cars' friction disk can deteriorate then

break. When it has deteriorated, chunks of rubber can separate and sometimes lodge themselves

between the disk and the flywheel, inhibiting normal clutching. The missing rubber can also produce

a noticable drivetrain vibration, typically aroung 3000 RPM.

If the rubber center breaks, all hope is not immediately lost. The friction disk has built into it a

limp-home backup. There are mechanical stops which will keep the splined tube and disk

connected enough for you to drive the car home or to the shop -- if you are gentle. You'll feel the

backlash as you hit the stops in either direction: accelerating or decelerating. These stops are not

terribly strong and can be destroyed if you drive aggresively on them.

Spring-centered clutches are not immune from failure. Their springs will break and, as with the

rubber design, will lodge in a way which disable the clutch. The original 944 Turbo friction disk also

had problem with its friction material separating from the backing plate. Porsche introduced an

improved design which includes adhesive bonding in addition to riveting.

10.0 Suspension and Related

10.1 I lost my wheel lock keys, what's the easiest way to get the lock off?

Either you can pay a locksmith a few bucks to pick the lock, or you can take a drill and drill out the

barrel of the lock. After drilling, the cover slides right off and you can remove the fastener like any

other lug nut.

10.2 What's the deal with replacement ball joints/suspension arms and what causes their failure?

Yes, ball joints are known to fail. However, it appears to occur mostly on lowered track driven

cars. Larger swaybars may also contribute. When the ride height is lowered a great deal, the ball

joint begins to reach the end of it's travel. Eventually the ball joint can crack, and then fail entirely -

possibly while you are driving very fast.

Assuming you're not doing any of the above (extreme lowering, larger swaybars, track usage) you

may want to go with a reconditioned/rebuilt arm if your ball joint fails. Several vendors do this,

including the pfiles recommended:

Dynamic European Technologies, Inc.

5103 Gulfton,

Houston, TX

713-661-2780

For the ultimate in control arm/ball joint assemblies, FABCAR offers their own fabricated arms with

a "replaceable monoball (spherical bearing)". These are the same arms that the IMSA requires on

any 944 racing in their series.

FABCAR

4385 West 96th Street

Indianapolis, Indiana 46268

317-872-3664

Fax 317-872-3835

The following is a statement released by Porsche Motorsports North America concerning the 944

Aluminum Control Arms:

To: all Porsche 944 & 968 Competitors

Re: 944 & 958 Control Arm Usage In Racing Applications

The following A arms should be installed in 944 and 968 Series vehicles according to the

conditions noted:

944 341 027 02 L/S Production version arm (round groove 360 degrees on ball

joint)

944 341 028 02 R/S Production version arm

These parts are good for moderate competition. (Time trials etc.)

951 341 027 32 L/S Competition version arm (slotted groove on side of ball joint)

951 341 028 32 R/S Competition version arm

These parts are recommended for long distance races or heavy competition.

Neither set of arms noted above pose a problem, as long as:

1.The ride height is not lowered beyond the point which causes binding of the ball joint when

the suspension reaches full travel,

2.The front sway bar is not greater than the M030 package sway bar in either 0.D. or wall

thickness,

3.The lower bore in the strut is not worn out and 4) the parts are assembled following the

steps outlined in the Porsche Service Manual. (Despite the fact that this may be slightly

contrary to the Service Manual, it is imperative that the bolt and nut (original Porsche Parts)

be replaced each time they are removed.

As always in racing, it is important to inspect the arms for nicks or cuts from road debris after each

event to avoid development of any cracks. Please note that the leading cause of failure we have

seen on both the Production and Competition version arms, in racing applications, is the failure to

follow the instructions I have listed above. Please call PMNA with any racing preparation issues.

Alwin Springer

Director of Porsche Motorsport N. A..

10.3 I could use some information about CV joints (failure mode, replacing, etc.), is there a FAQ about them?

Ed Gibbs (gibbs@avionics.itt.com) has written a nice little FAQ on CV joints on 944's. It can be

found at: ftp://ftp.mindspring.com/users/ccumming/Porsche/944/944.clu

11.0 Miscellaneous Engine Compartment

11.1 I have fungus/scum growing in my washer fluid reservoir/lines, how do I get rid of it?

Some suggestions from the list were: Remove and flush the washer reservoir once every year or

two. Perhaps add a drain hole to the bottom so that it doesn't involve removal.

There are also several commercial anti-freeze windshield washer solutions (including the Porsche

flavor that you can buy at your dealer) that contain methanol/alcohol/who knows what. They sound

nasty and will probably kill whatever is living in your tank while being reasonably safe for your car's

finish.

Another 'philer suggests that isopropanol and water would be the best/cleanest windshield cleaner.

Isopropanol is significantly more expensive than methanol which is probably why it's not used in the

commercial anti-freeze/deicers.

Other possibilities include a vinegar/water solution, or some of the chemical products used for killing

algae and bacteria in drinking water (RV and boat water tanks).

Things you probably don't want to run through your pump and washer system:

Diesel Fuel anti-bacterial/algae. It's greasy and nasty and would probably wreak havoc in your

system.

Bleach. Cleaning out the bottle with it would be OK, but running it through could cause nastiness to

your pump system and your car's exterior.

Simple Green. Some people use this with good success. However, several sources (including

Simple Green) agree that having it settle on your paint would probably be bad for both your wax

and even some finishes (dulling the paint and removing your wax). Using a low concentration and

making sure it's rinsed off fairly quickly would be a good idea.

12.0 Electrical

12.1 My antenna on my early 944 (the garden variety non-windshield antenna) is broken.  Where can I get a replacement and how do I replace it?

The original Porsche part is approximately $300 and can be ordered from many mail order places.

If you're not worried about originality, there are several non-Porsche power antennas that will work

in the $80 range. They don't fit exactly, but they do perform the antenna function.

To replace the antenna you need to remove the charcoal canister in the driver side fender and

unattach the hoses that connect to it. After getting the charcoal canister out of the way, you can now

see the antenna motor. The bottom of the motor is held in place by a nut and washer, the top is held

by a nut outside the car on top of the antenna. Carefully remove the nut and the entire assembly will

come free.

12.2 My AM radio reception is terrible, but FM seems to work fine, what's up?

Poor AM radio reception is typically caused by the pre-amp not receiving power. Apparently the

pre-amp is not required for good FM reception if they have fairly strong signals. The power to the

pre-amp is sent through a black wire in the same sleeve as the power antenna. +12 volts should be

applied to this wire whenever the radio is on. Most radios have a "Power Antenna" wire that should

work for this function. Directly connecting +12V would be a bad idea since it would eventually

drain your battery.

12.3 How do you remove the stock Blaupunkt radio?

As a security measure, the Blaupunkt radios are mounted in a special bracket with no obvious

means of removal. There are 4 holes at each corner of the radio face that are used to unlatch the

radio. Although there is a special "tool" available to remove the radio, the simplest way to use 4

pieces of stiff wire or nails. Simply insert them into the holes and the radio will come free.

12.4 Ignition wires are HOW MUCH!? What's so special about Porsche wire?

Nothing. Wire is wire. After a few years, the insulation breaks down and you get a pretty light show

under your hood from arcing (obviously, this is pretty bad for your ignition system). It is possible to

replace the actual cable while retaining the connectors. Normal ignition wiring will work fine. To

repair the wiring, unscrew each wire that has a threaded end. You can remove the old wiring by

picking it out after cutting it near the connector. After the connector is free from the old wiring, you

can drill a small hole into the base. Cut some bulk ignition wire to the proper length, strip off just

enough insulation to properly seat in the connector, and solder them together. Follow the same

procedure for the other end, rethread and tighten (you may want to add some dielectric lubricant on

the wire and cup, both Jim Pasha & Bruce Anderson recommend this stuff for any electrical work.

Porsche's factory response is that it's a no-no because it may gunk up and cause a poor

connection.) It is possible that you will destroy the connector in the process of rebuilding it, so you

may want to pick up a spare or two from a junkyard or dismantler.

12.5 Can I upgrade my headlights to something brighter?

One of the best lighting upgrade appears to be the Hella H-4's (sold for off-road use only, of

course). These are halogen based and come with 55/60 watt bulbs. Brighter replacement bulbs are

available. Be aware that in the U.S. you may be hassled by the police if you continuously drive

around with 100 watt laser beams of death. Hella lighting is available from most mail order houses.

Figure around $80-120 for the headlights, plus $15-30 each if you want upgraded replacement

bulbs.

The replacement bulbs include:

H-4 55/60 watt (comes standard with the headlights)

H-4 80/100 watt

H-4 55/100 watt

12.6 Where are good locations to install stereo equipment?

Amps

Under glove box.

CD Changer

Left or right rear storage compartments. The smaller six disk changers fit here nicely. Make sure the

changer you buy will work on its side/any angle to avoid mounting problems.

Since this subject is large enough to fill up the FAQ by itself, take a look at the car audio and

security information at http://www.mindspring.com/~ccumming/944corner.htm.

13.0 Performance Modifications

13.1 Chips/Chipping

If your car is new, Porsche's official response is that using one will void your warranty. The 968

(and 993) Bosch management system will lower the rev limit if it detects a non-factory chip installed.

The factory tends to underspecify their car's power slightly. Plus, chip vendors are usually highly

optimistic on their claims of power increase. Take their fancy chart-o-graphic specification sheets

with a grain of salt.

It's possible the chip is not smog legal in your area. It may also cause problems with the new

IM-240 "rolling" smog test, in which a fixed program of RPM ranges is used to give a more

accurate picture of your vehicle's emissions.

And remember: there is no free lunch. The factory did what it did for a reason, if there were an extra

20 hp that could be gained without any loss in flexibility, reliability or safety they would have used it.

Things a chip can do:

Increase throttle response by modifying the throttle profile (Turbo, 944S, S2, 968)

This similar to adding a round throttle cam to a regular 944. The normal throttle cam and throttle

profile are flatter when you first begin to accelerate. This helps prevent lunging and makes your

driving smoother. A modified throttle profile makes the response quicker - less pedal movement

equals more gas. No actual HP results from this, but it feels racier.

Increase Boost (Turbo)

Yes, increasing boost gives you more power. Possible damage could result, see below under

"Performance Gains".

Increase Rev Limit

This probably won't give you more power. It can come in handy when auto-crossing. It may allow

you to take a turn without up shifting where you normally would due to the rev limiter. On cars

where peak-torque is very high, it may also help your straight acceleration times if your power

doesn't roll off too steeply after a certain RPM. Normally the rev limit increase by these chips is

fairly small (for example, 500 RPM), so damage to your engine is unlikely if you use the extra revs

rarely.

Increase spark advance and/or lean out the mixture to use 92 octane gas

This sounds like the holy grail. Free HP, and all you have to do is use better gas! Well, yes. This is

where the chip-maker's claims usually stem from (as you can see, in non-turbo cars, the other items

aren't going to give you more actual power). However, most of the high compression cars already

require 92 octane gas. In older, lower compression cars, you're more likely to see some

improvement.

Performance gains:

Normally Aspirated Cars

Zero to minimal. Some chips will trade low-end torque for some loss at high end (minimal, in the 5

hp and below range). Damage is unlikely to result to your car, but the engine could be damaged if

the programmers were clueless like running the engine too lean which would lead to detonation

(knocking, pinging) and the subsequent engine destruction. You may also notice a slightly different

engine note because of the advanced timing.

Turbo

Yes, more boost = more HP.

With that being said, all the chips increase boost by controlling the waste gate. The factory tends to

roll off boost above ~4500 RPM to lessen the strain on the engine. The after market chips usually

increase both the over-all boost and not roll it off as much at high RPM.

However, the head gasket is not a strong point of the 951 engine. The factory has revised the part

several times, changed the torque values for the bolts, etc. Almost all the chips claim to have special

mappings for the engine control module that allegedly minimize the chance of gasket failure. Some

may be better at this than others. But don't fool yourself: running more boost puts more load on your

head gasket, the engine, and the rest of the car.

There are several after market suppliers that carry copper, stainless steel and other "exotic" head

gaskets. Replacing your head gasket and upgrading the bolts to something like Raceware fasteners

may allow you to run more boost without losing a head gasket - for a while. How long your rods

and bearings will last is questionable.

Kevin Gross has this wise advice (paraphrased):

"If you overboost the engine, or run the timing wrong or any of a number of sins, something's going

to break. Head gaskets are cheap and easy to replace. Holed pistons, burnt valves, etc., etc., are

expensive and difficult to replace. Think twice before compromising your 'safety valve' head

gasket."

15 PSI or 1.1 bar of boost appears to be the maximum amount of boost you can run with a

reasonable margin of safety. Going beyond this (such as the injectors maximum of 17 psi) would

require extensive modification such as replacing the fuel pump, seals, transmission to handle the

extra power, etc., etc.

If you must have a chip:

See if you can find a used one. Damage for the normally aspirated cars is unlikely to result, so you

might as well pick up a chip cheap. If you buy one new, make sure you buy from a vendor that lets

you return it "no questions asked". If the chip doesn't live up to your expectations, you can return it.

13.2 Engine & Transmission

13.2.1 Using a 944S ring & pinion in a 944 Turbo transmission.

The answer is: DON'T.

There have been many reports of 944 Turbo transmissions self-destructing because of this

modification. Basically, the 944S ring & pinion just can't handle the power of a turbo. So just say

no to this modification. It might be ok for street use, but a transmission rebuild is mighty expensive.

13.3 Lowering/Suspension

See section 10.2 for cautions regarding extreme lowering.

13.4 Wheels

13.4.1 What wheels and offsets fit where?

The following is included with the permission of Jim Pasha. This information was originally printed in

the June 1995 issue of Excellence magazine in the article "Wheels for the front-engine Porsche" on

page 107. The article contains much more useful information besides this chart, highly

recommended. Thanks to Jim for giving permission to include the chart in this FAQ. The chart is

pretty much unedited, besides removing the 928 information.

924/944/968/ Wheel and Tire Size and Offset Information

Year/Model              Original Tire Size                      Front                       Rear                       Wheel Size

924, 1976-84           4 bolt/108mm dia.(4.25")        165 HR 14              165 HR 14                    5 1/2 J x 14

185/70 HR 14        185/70 HR 14               6 J x 14 (alloy)

205/60 HR 15        205/60 HR 15               6 J x 15 (alloy)

Backspacing                                  Offset

110mm/4.33"                          33.8mm/1.33"

110mm/4.33"                          33.8mm/1.33"

110mm/4.33"                          33.8mm/1.33"

Year/Model              Original Tire Size                      Front                       Rear                       Wheel Size

924, 1979-84        4-wheel disc, 5 bolt/130mm     185/70 VR 15                 185/70 VR 15           6 J x 15

205/55 VR 16                 205/55 VR 16           6 J x 16

Backspacing                                  Offset

143mm/5.63"                          53mm/2.09"

143mm/5.63"                          53mm/2.09"

Year/Model                                                         Front                       Rear                    Wheel Size

944, 1982-86                                                  185/70 VR 15        185/70 VR 15               7 J x 15

215/60 VR 15        215/60 HR 15               7 J x 15

205/55 VR 16        205/55 VR 16               7 J x 16

Sport 1983 to 1986           front:                  215/60 VR 15                                              7 J x 15                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                              rear:                                                    215/60 VR 15              8 J x 15

Backspacing                                  Offset

125mm/4.92"                         23.3mm/0.92"

125mm/4.92"                         23.3mm/0.92"

125mm/4.92"                         23.3mm/0.92"

125mm/4.92"                         23.3mm/0.92"

112.2mm/4.42"                      10.6mm/0.42"

Year/Model                                                         Front                       Rear                    Wheel Size

944, 944S 1987-1988                                     215/60 VR 15        215/60 VR 15               7 J x 15

Sport   Front:                                         205/55 VR 16                                              7 J x 16

Rear                                                                          225/50 VR 16               8 J x 16

M030 Option    front:                                 225/50 VR 16                                              7 J x 16                                                                                                                                                                                                                                                                                                                                                                                                 rear:                                                                245/45 VR 165             8 J x 16

Backspacing                                  Offset

153.9mm/6.06"                           52.3mm/2.09"

153.9mm/6.06"                           52.3mm/2.09"

153.9mm/6.06"                           52.3mm/2.09"

153.9mm/6.06"                           52.3mm/2.09"

153.9mm/6.06"                           52.3mm/2.09"

Year/Model                                                         Front                       Rear                    Wheel Size

944S2 1989-1991                                          225/55 ZR 16                                              7 J x 16

245/50 ZR 16               8 J x 16

M030 Option    Front                                 225/55 ZR 16                                              7.5 J x 16

Rear                                                                 245/45 ZR 16               9 J x 16

Backspacing                                  Offset

143.9mm/5.67"                           55mm/2.17"

153.9mm/6.06"                           52.3mm/2.09"

160.25mm/6.31"                         65mm/2.55"

174.3mm/6.86"                           60mm/2.36"

Year/Model                                                         Front                       Rear                    Wheel Size

968 1992-1995                                              205/55 ZR 16                                              7 J x 16

225/50 ZR 16               8 J x 16

Clubsport          Front                                 225/45 ZR 17                                              7.5 J x 17

Rear                                                                 245/40 ZR 17               9 J x 17

Backspacing                                  Offset

143.9mm/5.67"                           55mm/2.17"

153.6mm/6.05"                           52.mm/2.05"

150.3mm/5.91"                           55mm/2.17"

166.3mm/6.54"                           52mm/2.05"

Year/Model                                                         Front                       Rear                    Wheel Size

924S 1986-1988                                            205/65 VR 15        205/65 VR 15               6 J x 15

Sport                                                      205/55 VR 16        205/55 VR 16               6 J x 16

Special M030   Rear                                                                   205/65 VR 15               7 J x 15

Backspacing                                  Offset

153.9mm/6.06"                          52.3mm/2.09"

153.9mm/6.06"                          52.3mm/2.09"

153.9mm/6.06"                          52.3mm/2.09"

Year/Model                                                         Front                       Rear                    Wheel Size

944 Turbo 1986                                            205/55 VR 16                                             7 J x 16

225/50 VR 16               8 J x 16

Backspacing                                  Offset

125mm/4.92"                             10.6mm/0.42"

112.2mm/4.42"                           23.3mm/0.92"

Year/Model                                                         Front                       Rear                    Wheel Size

944 Turbo 1987-1991                                  205/55 VR 16                                              7 J x 16

225/50 VR 16               8 J x 16

M030 Option        Front                             225/55 VR 16                                              7.5 J x 16

Rear                                                               245/45 ZR 16               9 J x 16

Sport/Club Sport: Front:                             225/50 ZR 16                                              8 J x 16

Rear:                                                              245/45 VR 16              9 J x 16

Backspacing                                  Offset

153.9mm/6.06"                            52.3mm/2.09"

153.9mm/6.06"                            52.3mm/2.09"

160.25mm/6.31"                          65mm/2.56"

174.3mm/6.86"                           60mm/2.36"

161.6mm/6.36"                           60mm/2.36"

174.3mm/6.86"                           60mm/2.36"

Note: While research has been done to verify all the dimensions in the table, there may be discrepancies between this published data and factory documentation. Listed information is based on actual measurements and some calculated data where an example wheel could not be obtained. Should you have any doubts, measure the wheel yourself for actual verification.

13.5 Brakes

13.5.1 My front brakes seem to be doing most of the work and wearing out twice as fast as my rears, can I adjust the front/rear proportions?

The answer is, yes, you can change the front-to-rear braking bias. Unless your name is Michael

Andretti, you have probably heard that many race cars have adjustable brake bias systems, which

their drivers use to tune the car's front-to-rear braking.

The 924S and the eight-valve, normally aspirated 944 was not equiped with a brake proportioning

valve. Because of this, the front-to-rear proportion was fixed, determined by two things:

the relative piston diameter of the front and rear caliper's pistons,

the relative bore size within the tandem brake master cylinder for the front vs. rear circuits.

The caliper piston diameters can usually only be known by taking off the caliper and measuring. The

front and rear piston bores within the brake master cylinder are usually stamped or cast into the

master cylinder. With the 944S, Porsche introduced a 33/5 proportioning valve. For the 944 Turbo

and 944S2, Porsche originally used an 18/5 proportioning valve, then later superseded it to the

same 33/5 valve used on the 944S and some 928-series models.

Why is braking proportion important? You may remember from your high school physics courses

that the frictive force generated by an object moving across a surface is directly proportional to the

weight of the object, that is, the force with which it pushes down on the surface. So if you double

the weight on a car's tire, it can grip the road twice a strongly.

For tires, the contact patch of rubber has a total limit to the force it can generate while still rolling.

This force depends on the weight on the tire: the more weight pressing a tire down onto the road

surface, the more force that tire can generate along the road surface. When this force is exceeded,

the rubber loses grip with the road surface and the contact patch slides along the road surface

instead of interlocking with it. The car's wheel stops turning and is said to have "locked."

Another important bit of physics takes place when you use your car's brakes: weight transfer. The

harder you use your brakes, the more weight is transferred to the front wheels and tires, and the less

weight is borne by the rears. This affects the braking force which can be generated: the less weight

on the rear tires, the less ultimate braking force they can generate before locking up.

So, it turns out that as you brake harder, it's best that the rear wheels do proportionally less of the

braking. Since it's hard to change caliper piston size on the fly, a proportioning valve does the trick

by instead reducing line pressure in the rear circuits. The chart on the right shows how this would

look ideally, rear pressure increase gradually rolling off as system pressure (pedal effort) increases.

A proportioning valve gives you an  approximation to this ideal curve, using two straight-line segments. Up to the point of the change-over pressure, both the front and rear brake circuits receive full system

pressure, i.e., the pressure within the brake master cylinder. Above the change-over pressure, only a fraction of additional system pressure is shared with the rear brake circuit.

There are two ways to affect the proportioning in your Porsche. By far the simplest, and perhaps

safest, is to add or change the factory-style proportioning valve, which threads into the brake master

cylinder's port for the rear circuit. The 33/5 designation on the valve currently used in 944-series

cars is decoded as follows. The "33" refers to a 33 bar change-over pressure. One bar is 14.5 PSI,

and so this valve starts reducing incremental pressure to the rear circuit when system pressure

exceeds 478.5 PSI. The "5" indicates a reduction factor of 0.46, so that each additional bar of

system pressure will add only 0.46 bar to the rear circuit's line pressure.

A second approach to modifying braking behavior is the installation of an adjustable proportioning

valve. These are commonly used in professional racecars, whose drivers will fine tune the change-over point to cope with changes in outdoor temperature, tire compound, track surface,and wet/dry condition.

Before you rush off to implement any of these features, keep a few things in mind. The first is that it

is perfectly normal for you car's front brakes to be doing most of the work. For this reason, you will

always go through front brake pads and rotors faster than rears. The only way to change this is to

reduce front-to-rear weight transfer under braking. And the only way to change weight transfer is to

alter the car's center of gravity, its weight, or its wheelbase.

Another thing to keep in mind is the effect of locking up under braking. For a pure racecar, the ideal

set-up is one such that the rears and fronts lock at the same pedal pressure. For a street car, and for

most track enthusiasts, biasing the set-up in a way which causes the fronts to lock a little sooner that

the rears is ideal. If your car locks its rears, it becomes extremely unstable in a hurry. Think of a

pendulum being held with its weight above its axis. If you lock the fronts but keep the rear turning,

you may flat-spot your tires and dampen your linens, but your car will remain controllable.

If you have the 18/5 proportioning valve on your car and switch to the 33/5 valve or an even more

radical valve used on late-model 911-series cars, you should be aware it may cause rear brake lock

up. If your car has ABS, some folks feel that the change is worthwhile and safe, especially for track

usage. However, others have expressed the fear that locking up all four tires at once would cause

the ABS system to think the vehicle is stopped. The p/n for the 5/33 valve is 928.355.305.02 and

lists at around $69.05.

14.0 924/944/968 Resources

14.1 Books/Recommended Reading

The Porsche 924/944 Book, Peter Morgan

Porsche 924 928 944, Jerry Sloniger

Porsche 924 and 944, Michael Cotton

The Illustrated Buyers Guide, Dean Batchelor, 170 p, 220 ill.

Porsche 924 and 944, Nigel Edwards

Porsche 944, Julian MacNamara

Porsche 924-928-944-968, David Vivian

Porsche Excellence Was Expected, Karl Ludvigsen

The Porsche Book, Lothar Boschen, Jurgen Barth

Porsche 968, David Sparrow/Adrienne Kessel, 128 p.

Bosch Technical Instructions:

Motronic (DME) Injection, Bosch, 44p, 101 ill.

Bosch Fuel Injection & Engine Management, Charles Probst, 192 p.

Porsche 944 Gold Portfolio 1981-1991, Brookland Books (magazine article reprints), 172 p.

Porsche 944 1981-1985, Brookland Books

Car & Driver on Porsche 1982-1986, Brookland Books (article reprints)

Road & Track on Porsche 1975-1978, Brookland Books

Road & Track on Porsche 1979-1982, Brookland Books

Road & Track on Porsche 1982-1985, Brookland Books

Road & Track on Porsche 1985-1988, Brookland Books

Best of Excellence "Technical Notes", Excellence Magazine

Jim Pasha's 924/928/944 series of articles in Excellence Magazine:

"So You Want To buy A Water Cooled Porsche", Feb. 94

"Hunting For Used Parts For Your 924/944/998/928", April 94

"General Suspension Preparation 924/944/968", May 94

"Motor Mounts And Exhaust Systems", June 94

"944 Timing Belts And Water Pumps", August 94

"924/944/968 Drivetrain Components", Oct. 94

"Brakes 924/944/928", Nov. 94

"Dealing With Electrical Problems In Water Cooled Porsches", Dec 94

"944 Series DME The Brain That Controls The Brawn", Feb. 95

"944 (and 928) Oil Systems, April 95

"924 Valve Adjustment, Axle Bearings", May 95

"General Maintenance - 924/944/928", August 95

"924 Brakes, Struts, and More", Nov. 95

"Frequent Questions: Front-Engined Porsches", Feb. 96

"944 Body & Front Control Arms", May 96

"944 Flywheel & Clutch", June 96

"924/944/968 Power Steering", August 96

"Cold Weather Maintenance", Nov. 96

Some Excellence Articles:

"Solid Value: Buying A Used 944", Bob Beebe, April 93

"Porsche Price Trends" $ 24,000, Bruce Anderson, Dec. 92

"944 Wheel Conversion", David Coleman, April 92

Import Motor Service:

"944 Common Repair Items", Ralph Birnbaum, April 93

PCA (Porsche Club of America) Publications:

"Up-Fixin" volumes 6, 7, 8, 9. These include all technical articles from Panorama. These particular

volumes cover the 924/944/968 series. There is also an index you can order along with these

volumes from Porsche Club of America.

PCNA Publications List 944/968 series: (924 list will be added soon) Note: The prices are not all

up to date and not all of these are still available from PCNA. These are great sources of info.

PORSCHE 944/968 SERIES PUBLICATIONS PRICE LIST

title                                                                           part number                                        list price, US$

Illustrated Parts Catalog, 924, 1976-79              WET 613 600                                                43.55

Illustrated Parts Catalog, 924, 1976-79              WET 614 000                                                43.55

Illustrated Parts Catalog, 924S, 1987-88            WET 614 400                                                43.55

Illustrated Parts Catalog, 944, 1983-85/1           WET 613 900                                                43.55

Illustrated Parts Catalog, 944/S/T, 1985/2-88   WET 614 300                                                49.77

Illustrated Parts Catalog, 944S2/T, 1989-91      WET 614 900                                                49.77

Illustrated Parts Catalog, 968, 1992-95               WET 615 000                                                43.55

Interpretation List                                                WET 603 114                                                   8.55

Microfiche, 944, 83-85                                         WET 613 921                                                   8.55

Microfiche, 944, 1985/2-88                                  WET 614 321                                                   8.55

Microfiche, 944, 1989-'91                                     WET 614 921                                                   8.55   Microfiche, 968, 1992-95                                      WET 615 021                                                    8.55

Maintenance Book, 944, 1983                            WKD 433 423                                                   1.00

Maintenance Book, 944, 1984                            WKD 434 023                                                   1.00

Warranty & Maintenance, 944, 1985                WKD 434 423                                                   1.75

Warranty & Maintenance, 1986                        WKD 900 023 86                                              8.55

Warranty & Maintenance, 1987                        WKD 900 023 87                                              8.55

Warranty & Maintenance, 1988                        WKD 900 023 88                                              8.55

Warranty & Maintenance, 1989                        WKD 900 023 89                                              8.55

Warranty & Maintenance, 1990                        WKD 900 023 90                                              8.55

Warranty & Maintenance, 1991                        WKD 900 023 91                                            10.30

Warranty & Maintenance, 1991, Supplement WKD 900 423 91                                                .85

Maintenance Manual, 1992                                WKD 900 023 92                                             8.55

Warranty Booklet, 1992                                      WKD 900 123 92                                             7.80

Maintenance Manual, 1993                                WKD 900 023 93                                             8.55

Warranty Book, 1993                                           WKD 900 123 93                                             9.91

Maintenance Manual, 1994                                WKD 900 023 94                                             8.55

Warranty Book, 1994                                           WKD 900 123 94                                             8.55

Warranty Manual, 1995                                       WKD 900 123 95                                             8.55

Tech Specs, 944 82-83                                          WKD 422 820                                                  8.55

Tech Specs, 944 84-89                                          WKD 423 320                                                  8.55

Tech Specs, 944S/S2/T                                        WKD 423 320                                                   8.55

Tech Specs, 968                                                    WKD 423 820                                                 12.85

Owners Manual, 944, 19                                      WKD 470 820                                                 20.50

Owners Manual, 944, 1983                                  WKD 470 821                                                 20.50

Owners Manual, 944, 1984                                  WKD 472 221                                                 20.50

Owners Manual, 944, 1985/1                               WKD 473 021 01                                            20.50

Owners Manual, 944, 1985/2                               WKD 944 021 85                                            25.65

Owners Manual, 944, 1986                                  WKD 944 021 86                                            20.50

Owners Manual, 944, 1987                                  WKD 944 021 87                                            20.50

Owners Manual, 944, 1988                                  WKD 944 021 88                                            20.50

Owners Manual, 944, 1989                                  WKD 944 021 89                                            20.50

Owners Manual, 944S2 1990                               WKD 944 021 90                                            20.50

Owners Manual, 944S2 1991                               WKD 944 021 91                                            20.50

Owners Manual, 968, 1992                                  WKD 968 021 92                                            22.50

Owners Manual, 968, 1993                                  WKD 968 021 93                                            22.50

Owners Manual, 968, 1994                                  WKD 968 021 94                                            22.50

Owners Manual, 944 Turbo S, 1988 OM Supplement    WKD 944 621 88                               1.75

Poster, 944 Engine, Side View (Illus.)                WKD 504 000                                                 12.50

Poster, 944 Trans Side View (Illus.)                   WKD 506 000                                                 12.50

Poster, 944 Turbo Eng, Front (Illus.)                 WKD 503 000                                                 12.50

Poster, 944S2 Engine, Long. Section (Illus.)    WKD 504 100                                                  12.50

Poster, 944S2 Engine, Trans. Section (Illus.)   WKD 503 100                                                  12.50

Serv Info, 944, 1982 (114 p.)                                WKD 450 621                                                    6.80

Serv Info, 944, 1982 (72 p.)                                  WKD 450 721

Serv Info, 944, 1983                                              WKD 450 921                                                    1.35

Serv Info, 944, 1984                                              WKD 490 121                                                    8.55

Serv Info, 944, 1985 DME Test                           WKD 450 821                                                    6.80

Serv Info, 944 Turbo, DME/KLR, 1985              WKD 453 920                                                    8.55

Serv Info, 944 Turbo, Info, 1985                         WKD 491 321                                                    1.75

Serv Info, 944, 1985/2                                           WKD 490 221                                                    8.55

Serv Info, 944, 944 Turbo '86, Servicing            WKD 492 020                                                    8.55

Serv Info, 944, 944 Turbo '86, Tech Info.           WKD 492 221                                                    8.55

Serv Info, All Models, ABS Brakes, '86             WKD 493 721                                                    6.80

Serv Info, 944 Diagn. Body Dam.                        WKS 502 021                                                    8.55

Serv Info, 944 Trans.                                             WKS 304 021                                                    8.55

Serv Info, 944 Series, 1988                                    WKD 494 221                                                   6.80

Serv Info, 944 Series, Air Bag Info '87                WKD 493 621                                                   6.80

Serv Info, 924S, 944, 944S, 944 Turbo '87           WKD 493 221                                                   8.55

Serv Info, 924S, 944, 944S, 944 Turbo '87           WKD 492 920 ??                                              8.55

Modifications, Data Settings, Wiring

Diagrams, Information Technic

Serv Info, 944S, '87 Servicing, Assembling       WKD 493 521                                                    2.75

Serv Info, 944S, DME Test Plan, 1987                WKD 494 121                                                    6.80

Serv Info, 944 Turbo S, 1988                                WKD 495 021                                                    6.80

Serv Info, 944 & 944 Turbo, 1989                        WKD 495 321                                                    6.80

Serv Info, 944S, 928S4 DME.LH-EZK                WKD 494 521                                                    6.80

Serv Info, 944S2 Cabrio, 1989-90                         WKD 495 721                                                    6.80

Serv Info, 944S2, 1989                                           WKD 496 021                                                    6.80

Serv Info, 944S2, 1990                                           WKD 496 221                                                    6.80

Serv Info, 944S2, 1991                                           WKD 496 721                                                    8.55

Serv Info, 944S2, Body Sealing                            WKD 497 321                                                   8.55

Serv Info, 968, Intro Book '92                               WKD 497 421                                                  17.10

Serv Info, 968, Intro Book '93                               WKD 498 021                                                    8.55

Serv Info, 968, Intro Book '94                               WKD 498 821                                                    8.55

Serv Info, Paint (Gen'l) Repair Info                      WKD 482 620                                                  74.70

Serv Info, Paint Repair n                                        WKD 491 920                                                   2.75

Shop Man, 924 vols. (1-4) Thru. Supplement #9        WKD 481 521                                       256.20

Shop Man, 944 Turbo (Thru. Supplement # 4)           WKD 482 220                                         81.99

Shop Man, 944, Vols. (1-6) Thru. Supp # 26               WKD 481 821                                       307.45

Shop Man, 968, (Thru Supp # 10)                                 WKD 482 820                                       307.45

Campaign Info,                                                       PNA 000 060                                                    21.10

Campaign Bulletins                                               PNA 000 060 A                                                 29.50

PCNA Publications Catalog                                 PNA 000 006

PCNA Fact Book, 1986                                         PNA 000 042                                                       7.95

PCNA Fact Book, 1987                                         PNA 000 050                                                       0.00

PCNA Fact Book, 1988

PCNA Fact Book, 1989

PCNA Fact Book, 1990

PCNA Fact Book, 1991

PCNA Fact Book, 1992

PCNA Fact Book, 1993

PCNA Fact Book, 1994

PCNA Fact Book, 1995

Sales Reference Guide

Sales Reference Guide, 1995

Dealer Directory                                                      PNA 000 045                                                     6.72

Tech Bltn Index thru 1989                                      PNA 000 018 B                                                 6.95

Tech Bltns, 11/84-85, Book "B"                             PNA 000 028                                                  16.00

Tech Bltns, 1977-1984, Book "A"                         PNA 000 056                                                   36.35

Tech Bltns, 1986 Only, Book "C"                          PNA 000 055                                                  18.00

Tech Bltns, 1987 Only, Book "D"                         PNA 000 062                                                   18.60

Tech Bltns, 1988 Only, Book "E"                          PNA 000 076                                                   14.20

Tech Bltns, 1989 Only, Book "F"                          PNA 000 082                                                   18.00

Tech Bltns, 1990 Only, Book "G"                          PNA 000 082A                                                23.95

Tech Bltns, 1991 Only, Book "H"                          PNA 000 082B                                                24.95

Tech Bltns, 1992 Only, Book "I"                            PNA 000 082C                                                24.95

Tech Bltns, 1993 Only, Book "J"                            PNA 000 082D                                               24.95

Repair Manual, 924, 1977-1982, microfiche            PNA 000 108

Repair Manual, 924 T, 1980-1982, microfiche        PNA 000 109

SRT Micro Set, 944                                                   PNA 000 115                                                       0.00

SRT Micro Set, 944                                                   PNA 000 116                                                       0.00

R/M micro Set, 944T                                                 PNA 000 126                                                       0.00

R/M micro Set, 944                                                    PNA 000 127                                                       0.00

Tool Catalog W/O Binder                                        PNA 721 032                                                     38.00

Tool Catalog Supplement 1                                     PNA 721 032 01                                                  8.50

Tool Update, #2                                                        PNA 721 032 02                                                  8.50

Tool Update, #3                                                        PNA 721 032 03                                                  8.50

Tool Update, #4                                                        PNA 721 032 04                                                  0.00

Dealer Price Book                                                     PNA DLR 008 93                                                0.00

Price Book Retail                                                      PNA RTL 008 93                                                 0.00

Dealer Price Micro                                                    PSM 000 001                                                       3.00

Retail Price Micro                                                     PSM 000 002                                                       3.00

Supersessions Micro                                               PSM 000 003                                                       3.00

1986 Product Knowledge Workbook, 944/944T

944 Workbook W/ Test Questions          PNA 000 046                                                       12.95

14.2 Book/Literature Sources

Classic Motorbooks, 1 800 826 6600

Automotion, 1 800 777 8881

Dragich Auto Literature, 1 800 328 8484

My Porsche, 1 800 655 3280

15.0 Copyright Notice

This compilation is copyright (C) 1996, 1997 Kevin Gross. It contains information takes from many

sources, and all original copyrights remain with their respective holders. Permission is granted to

freely distribute this compilation for non-commercial purposes. Permission to distribute this

document via any pay-for-use service must be obtained from the author, kgross@connact.com.

The original HTML format of this FAQ actively found on Kevin Gross' website was converted and compiled into .doc format by Ben McDaniel, waletail@sunset.backbone.olemiss.edu.